TENDER DOCUMENTATION

PUBLIC TENDER ACCORDING TO THE

OPEN PROCEDURE

No.

JN-B0454

Purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting

(by lots)

CONTENTS

1	INVITATION TO SUBMIT BIDS FOR THE PUBLIC TENDER	4

2	INSTRUCTIONS FOR MAKING BIDS	5

2.1	Contracting Authority of the public Tender	5

2.2	Legal ground	5

2.3	Basic rules of operation	5

3	SUBJECT OF THE PUBLIC PROCUREMENT	6

3.1	TECHNICAL REQUIREMENTS AND SPECIFICATIONS	6

3.2	LOT A	7

3.2.1	Specification of the basic offer for the lot A: Purchase and integration of the DSNG van:	7

3.2.2	OP.1  Option offer no. 1	15

3.2.3	OP2.  Option offer no. 2	16

3.3	LOT B	21

3.3.1	Specification of the basic offer for the LOT B: transmitting-receiving equipment:	21

3.3.2	OP3. Optional offer no. 3	23

3.3.3	OP4. Optional offer no. 4	24

3.3.4	OP5. Optional offer no. 5	25

3.3.5	Final acceptance of the transmitting-receiving equipment	25

4	BID DOCUMENTATION	26

4.1	General conditions for making bid documentation	26

4.1.1	Clarification to the tender documentation	26

4.1.2	Language	26

4.1.3	Marking	26

4.1.4	Contents of a bid	26

4.1.5	Alternative bids and variant bids	26

4.1.6	Validity of the bids	26

4.2	Documents in the bids	27

4.2.1	Data on Bidder and Bid	27

4.2.2	Contents of the bid documentation	27

4.2.3	Form »Declaration on acceptance of the public tender conditions«	27

4.2.4	Form of an OFFER that has to contain:	27

4.2.5	Pro forma Invoice	28

4.2.6	Bidder's “Statement on criminal offences from the first and the second paragraph of Article 42 of the Public Procurement Act (ZJN-2C)” – for a legal entity	28

4.2.7	Bidder's “Statement on criminal offences from the first and the second paragraph of Article 42 of the Public Procurement Act (ZJN-2C)” – for a legal representative	28

4.2.8	Form “Statement under the fourth paragraph of article 42 of the ZJN-2C”	29

4.2.9	Form “Bidder’s statements, given under criminal and material liability”	29

4.2.10	Bank Certificate of solvency	29

4.2.11	Warranty conditions of the Bidder	29

4.2.12	Declaration of the Bidder regarding the spare parts	30

4.2.13	Declaration of the Bidder - all the offered equipment is factory-new	31

4.2.14	Declaration of the Bidder regarding the software upgrades	31

4.2.15	Statement of the manufacturer or principal	31

4.2.16	Sample of the Contract	31

4.2.17	Guarantee for the seriousness of the bid	31

4.2.18	Declaration, stating the Bidder shall provide a Performance guarantee (for both lots)	31

4.2.19	References	31

4.2.20	Technical documentation	32

5	CONTRACT AWARD CRITERIA	33

5.1	CONTRACT AWARD CRITERIA FOR LOT A	33

5.2	CONTRACT AWARD CRITERIA FOR LOT B	33

5.3	TWO BIDS WITH EQUAL BEST EVALUATION RESULT	33

6	REVIEW CLAIM	34

6.1	Legal base and terms for submission	34

6.2	Method of submitting the review claim	34

7	FORMS	35

DATA ON BIDDER AND BID	36

Declaration of Bidder’s acceptance of Public Procurement conditions	37

Form OFFER – LOT A	38

Form OFFER – LOT A	40

Form OFFER – LOT A	42

Form OFFER – LOT B	43

Form OFFER – LOT B	44

Form OFFER – LOT B	45

Form OFFER – LOT B	46

Proforma Invoice	47

Statement on criminal offences from the first and the second paragraph of Article 42 of the Public Procurement Act (ZJN-2C)	48

Statement on criminal offences from the first and the second paragraph of Article 42 of the Public Procurement Act (ZJN-2C)	49

Statement under the fourth paragraph of article 42 of the zjn-2c	50

Bidder's Statements given under criminal and material liability	51

Declaration of the Bidder regarding the spare parts	52

Declaration of the Bidder regarding the spare parts	53

Declaration of the Bidder – all the offered equipment is factory new	54

Declaration of the BIdder regarding the software upgrades	55

Statement of the manufacturer	56

Statement of the principal	57

Sample Contract	58

Guarantee for the seriousness of Bid No...... – FOR LOT A ONLY	73

STATEMENT regarding the Performance Guarantee	74

Explanation of the Tender documentation No. JN-B0454	75

# INVITATION TO SUBMIT BIDS FOR THE PUBLIC TENDER

Radiotelevizija Slovenija, Javni zavod,  is in compliance with 1. passage (item 1) of Article 24 of the Public Procurement  Act (ZJN-2C),  inviting the Bidders to submit their bids to tender in accordance with the open procedure for:

the purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting

(by lots).

Bids in three copies (one original and two copies) must be sent in sealed envelopes to the address:

“Javni zavod RTV SLOVENIJA, KOLODVORSKA 2, VLOŽIŠČE, 1550 LJUBLJANA, SLOVENIA”, with the postscript: "DO NOT OPEN - FOR  TENDER - BID FOR TENDER NO. JN-B0454 – " tape based video archival system for intermediate video production“. The full address of the Bidder is to be written on the envelope.

The term for acceptance of bids is until 09.00 a.m. on 12 July, 2011. Bids received after that time limit will not be counted and will be returned unopened to the Bidders.

Public opening of bids will be on 12 July, 2011 at 10.00 a.m.  on the premises of Commercial Department of Javni Zavod RTV  Slovenija, at Komenskega Street 7 in Ljubljana.

Before the public opening of the bids the present participants of the Bidders have to hand over written authorizations for participation on the public opening.

Ljubljana, 15 May, 2011                                                       Commercial Department of

RTV Slovenija

# INSTRUCTIONS FOR MAKING BIDS

## Contracting Authority of the public Tender

Radiotelevizija Slovenija, Javni zavod, Kolodvorska 2, SI - 1550 Ljubljana

VAT No.: SI29865174; Corporate registry No.: 5056497

Bids will be appraised by the General Manager appointed Evaluation Committee. The Decision on the award of a Contract will be issued by the Director General of Javni Zavod RTV Slovenija. In the evaluation of the tender the commission will take account of the criteria that are the constituent part of the tender documentation.

The selected Bidder must enter into a signed Contract within 8 days after receiving the “Decision on the Award of a Contract”. In the case of a Bidder not entering into a signed Contract, the Contracting Authority will validate the guarantee on the seriousness of the bid.

The Contracting Authority reserves the right to vary from the published values and quantities when selecting bids, subject to available financial resources and actual needs.

In case of receiving incomplete bids, the Contracting Authority shall annul the tender. The Contracting Authority reserves the right not to choose any of the bids (according to Art. 80 of ZJN-2B).

## Legal ground

The Public Procurement of Javni Zavod RTV Slovenija (hereinafter referred to as: Contracting Authority) is carried out in accordance with the valid Public Procurement Act (ZJN-2B) and by-laws applicable and in accordance with the legislation being valid on the field of public finances and on the field that is the subject of this public tender.

## Basic rules of operation

Every Bidder’s attempt to affect the treatment of the Contracting Authority or decision on the selection shall result in rejection of his Tender.  The same applies to all attempts related to the work and decision of the Evaluation Committee.

In the period from the publication until the conclusion of the Contract the Bidder shall be not allowed to commence and perform any actions, which might prior determine the selection of a defined bid. In the period from the selection of a Bid until the Contract comes into force the Bidder shall be not allowed to commence any actions, which might cause the Contract to become void and unfulfilled. In case the procedure is stayed the Bidder shall not commence or perform any procedures, which might aggravate the invalidation or objectivity of the Review Commission.

# SUBJECT OF THE PUBLIC PROCUREMENT

The subject of public procurement is DSNG vehicle for satellite transmiton of the TV video and audio signal to the RTV Slovenija premises or to another demanded location. DSNG van will be used for the  up link of contribution-quality TV signal, which is convenient  for further editing or archiving ,  for satellite transmition of  the news gathering, as two-camera production van. Must be designed for SD SDI and HD SDI video and AES audio production and transmition. DSNG van must be prepared to accept the analog TV signal as the source to the van system.

The tender is split up into the following two Lots:

- LOT A:  Purchase and integration of the DSNG van

- LOT B:  Transmitting - receiving equipment

Optional offers:

The Bidder has to offer separately from the basic offer of Lot A and B also the values of the optional offers, according to the requirements in items 3.2 and 3.3.

All the Contracting Authority’s technical and quantitative requirements for optional offers are in the tender documentation text marked with blue color and are in the technical specifications reasonably  added to the end of  textual statements  of the each connected particular basic requirements .

All optional offers must be obligatory.

## TECHNICAL REQUIREMENTS AND SPECIFICATIONS

The offered equipment has to operate according to the PAL standards, SD (576i at 50 Hz) and HD (720p/1080i at 50 Hz):

-  ITU-R BT.470-6

-  ITU-R.BT472

-  ITU-R BT.601/65, audio embedding SMPTE 272M

-  SMPTE 292M-1998, audio embedding SMPTE 299M

-  SMPTE 424M

-  AES-3-1992

-  AES-11-1997

All equipment powered by 230V AC must satisfy  acts and regulations valid today in the republic of Slovenia to do with  electrical powering (230V, 50 Hz)  and safety against electrical shock in accordance with SIST EN 50160,  SIST EN 60950.

Offered equipment must conform to EMC standards:

-  SIST EN 50081-1:1995

-  SIST EN 50082-2:1997

-  SIST EN 55022-2000

-  SIST EN 55024:2000

## LOT A

PURCHASE AND INTEGRATION OF THE DSNG VAN

The bid under the lot A must include all items from the table: »Specification of the basic offer for the lot A: Purchase and integration of the DSNG van«. The price of each item must be given separately.

Optional offers 1 and 2 are obligatory and include equipment to be integrated into the vehicle.

In case the Contracting Authority decides for the purchase of one or more options already at the Decision on the award of a Contract, the same will be included in the basic Contract. In case the Contracting Authority decides for the purchase of optional offers later   (in the period of one year from the beginning of the Contract validity, subject to available financial resources and actual needs), the contractual parties shall conclude an Annex to the Contract JN-B0454.

In case, that the option 1 and option 2 won’t be bought with the Lot A, the equipment described in the options 1 and 2 of the lot A, will be delivered to the chosen bidder of the  lot A for integration from the Contracting Authority.

### Specification of the basic offer for the lot A: Purchase and integration of the DSNG van:

| Specification of the basic offer LOT A – Purchase and integration of the DSNG van | qty |
| --- | --- |
| 1 | Vehicle Panel Van, 5t | 1 |
| 2 | Vehicle coachwork | 1 |
| 3 | Electrical system | 1 |
| 3A | Generator | 1 |
| 3B | UPS system for redund. powering of both RF chains for 10 minute | 1 |
| 4 | Air conditioning system | 1 |
| 5 | Antenna system | 1 |
| 6 | Installation of the transmitting-receiving equipment | 1 |
| 7 | Video/audio installation | 1 |
| 8 | Engineering, technical documentation | 1 |
| 9 | Visiting , factory acceptance, commissioning of the vehicle at integrator location | 1 |
| 10 | Final acceptance, user training on location of the Contracting Authority | 1 |

- The vehicle’s technical requirements

The bidder is obliged to provide the certificate of homologation for the van with modification.  The condition for getting the homologation is fulfilling the requirements of the Slovenian legislation for such vehicles. We suggest to the bidders to contact the provider of the homologation certificate  in Slovenija (f.e. http://www.rti.si )   when the coachwork project documentation is prepared to get the confirmation  that the coachwork will be according to the Slovenian law requirements.

The bidder has to provide documents, which confirmed the harmony with the European standards for

- Ecology ( noise, exhaust gas composition, coachbuilding material…)

- Driving (pressure on the axe, overall weight, dimension, braking system, pneumatic  parameters)

- Security (during the driving, when making a halt, during the TV production)

- Fire precausions

The offered vehicle has to be sold with the European registration certificate, valid in EU.

The offered vehicle has to operate in outside temperature range from  -30° to +40° C.

The modified vehicle with all the installed equipment, mentioned in this tender documentation, with accessories, cables and two passengers must not exceed the allowed gross vehicle weight. The weight calculation of the finished vehicle with modification, installation and passengers must be obligatory attached to the bid.

Panel Van (model example Mercedes Sprinter 519 or similar)

- length: max. 6150 mm

- height: max 3300 mm total with antenna system

- width: 2100 mm (side mirrors not included)

- colour:  arctic white

- high-roof model, height 2820mm, internal height minimum 1800mm

- »medium« wheelbase minimum 3665 mm

- vehicle length max 5910 mm without rear step

- cargo space minimum l x b x h [mm] 3265x1780x1840

- gross vehicle weight rating 5000 kg

- max. payload over 2500 kg

- 4-stroke diesel engine (water-cooled) with turbocharger displacement 2500 – 2999 cm³

- rated output higher than 135 kw

- rated torque [nm/min] higher than 400/1600-2600

- generator output  minimum 14V/150A

- battery    minimum  ca. 12V/100Ah

- fuel tank capacity  minimum ca. 75 l

- front and rear suspension upgrade

- 6 step  gear-box (6-speed manual transmission)

- adaptive ESP® in conjunction with anti-lock braking system (ABS), acceleration skid control (ASR), electronic brake force distribution (EBD) and Brake Assist (BAS)

- power steering (left)

- adjustable steering wheel

- hydraulic dual-circuit braking system with all-around disc brakes

- shock absorbers, strengthened

- sliding door for cargo bay -cabin (right) with window  with thermo-insulated double tinted glass

- all other windows with thermo-insulated gradual tinted glass

- rear doors, wide-opening (270 degrees), blank  without windows, with storage compartments inside

- radio with RDS , CD player unit, navigation

- »comfort interior cab equipment«

- central locking, internally-operated, remote

- exterior mirrors, electrically adjusted and heated

- air-conditioning, temperature-controlled

- parking and manoeuvreing assist system with rear camera

- on-site interior heating (like webasto or similar), precisely controllable heating and ventilation system, automatic control with programmable clock

- heated front window glass

- instrument cluster with clock and outside thermometer display etc

- xenon lamps with curve following lighting feature

- fog lamps (halogen)

- tyres for the season of delivery

- front and side airbags for driver and co-driver

- co-driver seat of comfort type for one person

- multi adjustable »hydraulic« driver's seat with elbow-arm and head support, seat belts

- rotatable driver and co-driver seat

- reading lamp for co-driver

- electrically controlled and heated exterior rear-view mirrors

- entrance lighting for driver / co –driver / sliding door

- on-side entrance step with electrical support

- step at rear doors

- 2 hydraulic stabilising feets

- upgraded Stabilizers on front axle

- Air Cushion on rear axle

- tempomat

- tachometer

- Speedometer,  Fuel Gauge, Quartz Clock …

- Indicator lights for turn signal indicators, main beam, charging current, oil level, coolant level, brake fluid and brake pads, etc.

- The vehicle coachwork comprising:

Internal  (operator area)

- 3 x 19” main racks (lay out drawing attached) mount across width of vehicle over rear axle

- At least two 19” subracks above main equipment racks up to the ceiling

- 1 x 19’’ half rack table of the height cca 75cm, which top will be used as an operating desk for lap top editor  or any other equipment, f.e. camera for inserting any format of recording into the vehicle system. Operater will be seated on the driver seat, turned around for 180°. Desk must have the folded extension over the operator’s legs, when working. The half rack table must include three shelves and three drawers

- wood finish operator desk in front of all 3 main racks, depth 60cm

- blackout curtains on all windows

- first air conditioning system for racks (Truma type built in the rack) and  high capacity high efficient air exhausting system  from  the back side of racks to outside of the van

- second cabin air conditioning system, ceiling type, built on the van roof

- air conditioning and heater temperature control for cabin must be  separated from the control for equipment  air conditioning for racks

- soundproofing and luxury finish to walls and ceiling

- non slip, antistatic and easy to clean floor

- DC (emergency) lighting and AC lighting with dimmer control (general illumination, working lights above desks)

- generator control, DC and AC monitoring , generator regulation

- AC outlets (at least three fused 16A outlets)

- system controller with visual and audible alarms for antena, jacks, doors, generator, ancillary inputs

- 2 operator seats with transport locks

- safety lock for right sliding door

- safety pack comprising antena lightening, internal front and rear smoke alarms, rear carbon monoxide alarm, fire extinguisher-CO2,  first aid kit,  low fuel warning

- providing the reinforcement on the wall above the half rack for the later monitor arm fixing

- all equipment installed in the van must be fixed to prevent it from the sliding during the driving

- detachable safety net for main eguipment racks, if the homologation provider demand it

Internal (rear storage area)

- shock/vibration proof generator mount

- high impact flooring

- composite sound proof quick release panels to rear of racks

- power interface panel with 5-pole 32A   input socket (for three-phase mains connection) 1 x32A for one- phase mains connection and two fused CEE 16A outlets

- A/V rear termination panel for video and audio (22x BNC, 32x XLR, 2x triax Fisher, 2x fiberoptic connector with loop across the fiberoptic to SDI receiver module back to 2x BNC on rear termination panel)

- first rear shelf with fixings  (anchor points) for the cargo tie down assembly (webbing and ratchet strap included), located  above the generator

- second rear shelf  with fixings  (anchor points) for the cargo tie down assembly (webbing and ratchet strap included), located cca 600mm above the first shelf

- 2 lightweight plastic removable cable reels with 100m of triax cable, fixed with webbing while driving

- 1 power cable reel with 50m of  power cable 5x2,5 square, 400V

- AC and DC lighting

- safe acces to the upper storage area for the operator must be enabled by the standing on the step, which can be folded,  on the rear edge of the floor in front of  the rear door

External

- electric or hydraulic rear support jacks controlled from operator area

- side and back lights

- rack ventilation air inlets

- folding awning, mounted above right sliding door

- folding awning, mounted above rear door

- mounting of the rear drive assisting camera made according to the folding awning

- roof lead through for cable set for control, RF, power

- cable entry point (flap) in right  rear door

- roof ladder mounted on the rear door, outer side, with covering

- mounting of the RF antenna with both HPA’s in the base of the antenna,  mounting of a receiving antena

- mounting of roof mounted cabin air –conditioning, cooling radiator for the generator, 3x GSM antennas, 2x intercom antennas, 2x audio monitoring – listening antennas

- mounting kit, prepared for mounting the mast, manually controlled,  outside the van

- all modifications made by the DSNG constructor of the basic vehicle have to be made strictly in accordance with the vehicle constructor’s recommendations

- paint refinishing in original colour

- Electrical system

12 kVA  generator built in super silent Fisher panda housing

- diesel engine

- self excited, brushless alternator

- output voltage 230V +/-1%, 50 Hz

- built in electronic control of the output voltage level (adjusting range +/-2% of 230V)

- water-cooled

- super-silent high level exhaust system

- thermostatically controlled roof mounted  radiator cooling with fan for generator cooling

- generator operates from vehicle tank

- 12V generator cranking battery

- remote control panel, fuel pump, fuel filter, muffler etc.

- Fuel entrance system to the generator must not allow the consumption of all the fuel from the tank

- accurate digital indication of remaining fuel

12kVA Isolation transformer (3 phase input, 1 phase output)

UPS system for emergency powering of both RF up-link chains for 10 minutes, double conversion, online UPS technology system, which totally isolates the load from the primary AC line.

12V DC system

- DC 12V battery, minimal 95Ah

- DC 12V automatic battery charger

- Switch-off for battery protection

- DC power distribution unit with main switch for 12V accessories and as many outlets as there are necessary

- DC voltage/current meter

- Battery monitoring with acoustic and visible alarm facility

Main power system

- the DSNG van must be designed for three-phase and for one-phase mains connection with maximum electric-shock protection

- Power input panel  inside the rear stowage area with CEE 3x32A  plus 1x32A internal connectors, both input connectors must be equipped with at least voltage and frequency meter, three-phase connection measurement for each phase separatly

- connection to the mains and to the generator must be done through isolation transformer with insulated case (12kVA / 3 phases input, one phase output) with input-voltage preselection (380V / 360V / 400V / 230V –by means of jumpers) and transformation to the secondary voltage of 230V

- Earth distribution point

- two output sockets CEE 16A for lighting powering

- each mains outlet must have individual circuit breaker FID (RCD)

- voltage, current, power, frequency presence display per phase and for generator power in the operating cabine

- main selector switch mains-off-generator

- mains ON/OFF switch panel with main fuse FID (ELCB) and main switch

- according to the law of electric energy supply, an appropriate power consumption measurement by means of an attested counter will be build in the mobile cabinet by the consignee after the delivery of the vehicle.

- Air conditioning

- Two air conditioning systems, built in by coachworker, are required, one for racks and one for the operator area- cabine

- must operate independently one form another, each with its own control

- assembly roof mounted air-conditioning should be used for cabine

- rack-mounted air conditioning system should be used for racks equipment

- the air-conditionig must be designed for external temperatures between –25 °C and + 40°C,

- internal temperature must be maintained between +18°C  and +24°C, user adjustable

- temperature must be adjustable by temperature-control sensor, separate for cabine and separate for the racks with equipment

- the operating area should be cooled indirectly through the ceiling, the environmentally and health-friendly methods must be used for cooling

- racks must have special high capacity ventilation to outside

- floor heating system for cabine is required

- Antenna equipment

Two RF transmittion chains must be installed in the vehicle, main and redundant with automatic change over. Complete full redundant satellite uplink system must comprise Ku band antenna, two linear waterproof high power amplifiers, two Ku band block upconverters, all necessary waveguides, low noise blocks, antenna controller and redundant controller, all necessary splitters, dummy load, cables, HPA changeover unit and control

- Transmitter frequency band: at least 14.00 to 14.5 GHz.

- Proposed antenna should have dimension (diameter) not less than 1,6m with mid band gain of 46 dB or more.

- Antenna feed should be at least dual port to enable reception (cross-polarised to transmit) in frequency band 10.70 do 12.75 GHz.

- The antenna steering must be motorised with manual control. The data about angular adjustment, azimuth, elevation and polarisation must be given.

- 2 pieces of HPA, main and redundant must be  located on the roof, integrated in antenna system.

- Each HPA should have output power at least 400 W.

- There should be possibility to switch over any HPA output to the dummy load.

- Patch panel (L band) should enable connection to the IRD and Spectrum analyser simultaneously.

- The existing spectrum analyser Rhode Schwarz type FS3 in rackmount version will be delivered to the chosen bidder for the  integration into the SNG van.

- Patch panel should enable local monitoring of transmitter signal either by means of L band monitor output from Up Converter or by means of Loop Down Converter without influence to the transmit signal.

- an another Rx chain with separate motorised pan and tilt antenna for reception of DVB-S TV programs transmitted from Hot Bird 3, with IRD capable to accept Viaccess conditional access card is required.

- The RF wiring schematic must be provided by bidder in the bidder documentation

- All equipment must meet the requirements as set in the Regulations on Technical Requirements for Radio Equipment published in the Official Gazette of the Republic of Slovenia No.50/97 from year 1997 and in the Regulations on Electromagnetic Compatibility, published in the Official Gazette of the Republic of Slovenia No.132/06 from year 2006.

- Prior to putting the radio stations into operation, the Provider shall acquire the Decision on Approval  required according to the Regulations on Determining Compatibility and for Approval of Terminal Equipment and Radio Stations (Official Gazette of the Republic of Slovenia No.50/97 from year 1997).

- Installation of the transmitting - receiving equipment

- Two RF chains must be installed, main and redundant with automatic change-over. The both RF chains must includes the coder/modulators of the newest generation.

- The redundant chain must be capable to simultaneously  transmit the another stream than the main chain.

- installation of two encoders/modulators and two receivers must be done

- Integrated encoder/modulator ,MPEG-2 SD and MPEG-4 SD, 4:2:2 and 4:2:0, DVB-S/S2, Q/8PSK software up-gradeable to HD, must ensure the broadcast contribution quality of the TV signal  for studio program exchange.

- receiver/demodulator MPEG-2 and MPEG-4, 4:2:2 and 4:2:0, DVB-S/S2, Q/8PSK, HD/SD SDI,

- bidder of the vehicle from lot A must offer the encoder/modulator and receiver,  described in lot B of the same tender

- detailed requirements for the encoder/modulator and receiver are described in the same tender documentation under lot B

- Video/audio installation

The supplied equipment to the chosen bidder.

RTVSLO as the Contracting Authority will supply some existing video/ audio equipment (exactly specified below)  to the bidder, who is obliged to integrate it  into the vehicle.  The equipment will be send to the integrator one month before the delivery time of the DSNG van  or on the  date  agreed on both sides.

If  the chosen bidder  will not be from EU, he has to take care for temporary import of the items.

Video equipment for DSNG

The video and audio equipment is seen on the attached basic  video and audio schematic (technical attachement no. 1 and 2). The final video and audio schematic must be provided by bidder, any better solution in wiring will be considered and approved by the tenderer, if acceptable.

The data, tally wiring is not drawn, schematic  must be provided by bidder in the bidder documentation.

The idea of rack layout is attached (technical attachement no.3). The final layout must be provided by bidder, any better solution will be considered and approved by the tenderer, if acceptable.

If  the offered solution with proposed changes will not be accepted and approved in writing by the tenderer, the required solution from the tender documentation must be realized.

Installation must be done with 3G coax cable.

Existing video Equipment, delivered to the bidder and must be installed in DSNG van is written bellow under items 1 to 9 below:

- Triax HD camera

1piece—HXC-100PK//U camera head

1piece—HXCU-100//U camera control unit

1piece—RCP-1500//U remote control panel

Camera sources in SNG van

One Sony camera in triax version (configuration HXC-100PK//U with HXCU-100 CCU, HDVF-20A VF, RCP-1500//U joystick control panel, Beyer dynamic DT-108 single ear headset for intercom with 5 pin XLR plug and cable ) will be delivered to the bidder for the installation into the van as the camera 1. CCU mounting in the rack, camera control panel mounting in the right  desk in front of the third rack is required..  The wiring, triax from termination panel to the CCU1, coax from CCU1 to the router and video mixer, return picture, tally wiring, control panel  wiring must be installed.

The second camera of the same type as the first camera will be used in the van occasionally when  required. It will not be delivered to the bidder. The camera head , CCU and control panel will be occasionally mounted into the van. Bidder has to prepare  the location and mounting adapters for CCU2 and for camera control panel 2. All the wiring provided for the camera 1 has to be provided also for the camera 2 ( triax from termination panel to the CCU2 location beside CCU1 location, coax reference in, coax from CCU2 location to the router, return picture, tally wiring, control panel  wiring). Fisher Triax connectors have to be installed on the rear termination panel for connection of both triax cameras.

Both cameras will be occasionally used as an external controlled cameras for the another production van, what means, that the both cameras CCU video outputs and tallies have to be available on the DSNG van rear termination panel for connecting to the  another production van.

Other external sources in SNG van from rear termination panel to the router

2 HD/SD  SDI external video lines from the rear termination panel to the router inputs are required for connecting of other production vehicles or other HD/SD sources (camcorders) .

2 Analogue external lines with integrated processing capability of format conversion PAL to SDI, frame synchronization and embedding the audio are required.  Any format of the video signal (analogue PAL, SDI, HD SDI) must be able to be connected to the module with processing capability, any processing stage or combination must be able to be enabled or disabled by web browser, depending of the requirements.

Internal sources – recorders, servers

Because of the different recording formats used on RTV Slovenija and possibility of interesting third party flash recordings, used for news gathering, wide range of formats have to be available for playout, permanently SxS card, DVCAM, DV,HDV playout, occasionally XDCAM PD, IMX, server in the future

Two locations are intended for the installation of the recorders and servers.

First location is in the  rack 3 for two  recorder/players which will be installed permanently into the van from the early beginning. They are both half rack wide and can be mounted side by side:

- Recorders

1 piece  PMW-EX-30 solid state recorder, player

1 piece  HVR 1500A  HDV, DVCAM, DVCPRO recorder, player

Second location for recorders is in the half rack 4, where the coax cable with BNC connectors and  audio cables with XLR connectors have to  be prepared for four times playout , two times for sync reference in and two times for recording. The cables should be twisted on the back of the half-rack 4 and will be connected to  any recorder or server which will be installed into the half-rack 4 later, for example the future XDS-PD1000, featuring SxS memory card slot, a professional disc and internal SSD storage, J-30 SDI MPEG IMX, BETACAM SP, BETACAM SX, DIGITAL BETACAM  player or any other required. The worktop on the half-rack 4 can be used for the laptop editing or as a place for any consumer camcorder to be connected to the system (entry point for it).  I-link  (IEEE 1394) transfer has to be enabled  between PMW-EX30 and HVR- 1500A in rack 3 and any occasionally used device with I-link transfer capability on half-rack 4 ( fire-wire cables prepared with connectors on both side).

Half rack 4 must be delivered with three shelves and three drawers, which can be simply user repositioned regarding to the momentary equipment installed in. The drawers must have a locker to prevent the opening  when driving.

- 3G Embedded router Miranda 32x32

1piece—CR3232-3GIG HD SDI video router, 2RU

1piece—RP16 remote panel expansion kit

1piece—CRPS1 redundant power supply

1piece—CP3201 32x1 button panel 1RU(require RP16)

1piece—XY buton panel for 2RU router chassis

HD/SD SDI 3G Miranda 2RU video router 32x32 with XY control panel on the router electronics must be located on the handy operating position in the rack 2.  1 separate button per source control panel will be used for selection the sources going to the measurement instrument WFM. The inputs and outputs of the router must be connected to the 3G Canare patch panels with 24 normal through patch plugs. All the wiring must be 3G capable

- Multi-image processor Miranda Kaleido

1piece—16 HD/SD SDI inputs

1piece— redundant PS

1piece—2 HD-SDI outputs

1piece— HD7SD-SDI embeded audio license

HD/SD SDI  Miranda Kaleido-X16-D Dual head Multi-image processor with 16 HD/SD SDI inputs, redundant PS, 2 HD-SDI monitoring outputs, HD/SD-SDI embedded audio license  will be used for monitoring of the sources, connected to 3G router.

Configuration of the displayed pictures will be preprepared for any mode of van operation and easy changed.  Multiview  output will be connected to 20’’ LCD monitors, installed in the racks 1 and 3, above the audio mixer and camera control. Monitors must be mounted on the hinges, in the way which  provides the possibility to mount the other rackmount units into the racks behind  the rear side of monitors.

- Waveform monitor Harris TVM9100PKG

1piece—TVM 9100PKG

1piece—TVM-A3-OPT 2 advanced audio analysis option

1 piece   HD/SD SDI  vaweform monitor Harris TVM 9100PKG  is half rack wide and will be delivered to the chosen bidder for installation into the rack next to the spectrum analyzer described below.

- Spectrum analyzer Rohde&Schwarz

1piece—FSC3 9kHz to 3GHz spectrum analyzer

1piece—FSC-B22 RF preamplifier

1piece—dual rackmount kit

- Video production switcher FOR-A

1piece—HVS-300RPS HD/SD video switcher with redundant PSU, 4SDI inputs w FS and upconv.,  16ch multivieuwer w/ tally@umd

1piece—HVS-30OU operator control panel

2pieces—HVS-30HSDI  SDI 4input card w FS and upconv.

2pieces—HVS-30HSDO  SDI 2 output card and downconverter

Video mixer  FOR-A HVS-300HS  has 12 inputs and 10 outputs.

Main PGM output and PGM bus will be used for transmition over the first RX chain, the AUX3  output from the second  output board with control over the AUX row of buttons on the main video mixer control panel will be used for transmittion over the second RX chain.  Video mixer will enable the mixing of the cameras  and VTR or server recordings playout, combining the HD and SD sources in HD mode of operation, as it  includes the converters on inputs. Internally generated black and test signals, still stores will be connected to the router via mixer AUX output. Video mixer provide the multiview monitoring output which will be connected to the 20’’LCD monitor in the rack 2, above the mixer control.

- Sync generator Rosendahl

1piece—Nanosync HD

HD/SD SDI Video SYNC generator Rosendahl with PAL black burst  and audio  sinhronization signals word clock and LTC will be used for synchronization of the SNG van equipment.

- Canare video 75OHM patchbays 3G

4pieces of standard size DVJ 24W normal through will be delivered to the bidder.

Tenderer's requirements for the options of the lot A

Video Equipment under options 1 and 2 must be offered by the bidder of lot A and installed in DSNG

### OP.1  Option offer no. 1

MODULAR EQUIPMENT

modular equipment of broadcast range (embeders, deembeders, converters, DA, FS,DA...) which are needed, as seen on video and audio schematics  must be offered. Modules, which are part of the up-link transmition line have to be 3G compatible or 3G ready, with the software upgrade possibility to 3G. The price of each module and chassis of the modular equipment must be specified in the offer. Each chassis has to include the redundant power supply. The spare power supply must be included in the offer which can replace any of the installed PS. The modular equipment with minimal space consumption is required, 4RU are available for modules and at least 3 spare slots for future modules must stay free(Lynx 5000 range or equivalent). 3G compatibility is required for modules,   where written in the table rows . Web browser control, SNMP monitoring of the modules have to be provided on the PC notebook, installed in the drawer in the rack.

| Module | Qty |
| --- | --- |
| 19" Rack Frame for 10 CardModules with fan front cover + Primary PSU+redundant PS | 2 |
| 1,5G 1>8 Wide Band Analog Video / Sync Distribution Amplifier | 2 |
| 3G/HD/SD 1>8 SDI Distribution Amplifier | 2 |
| 3G/HD/SD 16 Channel Embedder or De-embedder (selected an embeded function) - SubD balanced | 2 |
| 3G/HD/SD 16 Channel Embedder or De-embedder (selected a deembeder function)) - SubD balanced | 2 |
| SDTV Analog and Digital multifunction Processor (PAL-SDI conv.,emb,FS) | 2 |
| 1,5G SD/HD Monitoring Down converter with Analog and Digital Audio / Video Outputs | 2 |
| HD/SD SDI and AES Test Signal Generator with two test outputs, static and dynamic patterns, EBU A/V sync pattern for transmition alive, audio lip sync pattern | 1 |

Beside the modules required in the table the producer of the modules must produce also the following type of modules in the same module line. They are intended to be bought later and will be installed in the same rack frame (chassis):  HD/SD Up/down/cross converter module, 2 channel (2xAES) tracking and programmable digital audio delay module, 2channel change over  switch module, passive fiber multiplexer CWDM and optical splitter.

The availability of all required modules must be proved with published technical data of the modules on the producer web page.

Operating and service manual must be delivered with the equipment.

### OP2.  Option offer no. 2

LCD MONITORS

In each of the three main racks in DSNG vehicle one 20’’ monitor will be mounted.

Sample type DT-V20L3G or similar.

Technical requirements for 3G/HD/SD SDI LCD monitor:

- Colour temperature of the picture on the screen must be 6500(K (D65).

- The diagonal of viewable area must be at least 20”

- It’s width must not be more than  19( rack

- The angle of view (H and V) must be at least 178( or more

- Monitor must have at least 1600 x 1050 pixels

- Monitor must be possible to genlock to external video signal (PAL)

- Monitor can  have aspect ratio of the screen 16:10, but it must be capable to display geometrical non distorted picture with aspect ratio 4:3 and 16:9

- It must have less the one frame picture latency

- Monitor must have the possibility to use different markers (centre, safety cone and aspect)

- Monitor must have HD/SD-SDI INPUTs (at least A/B inputs)

- It must have DVI-D input

- It must be capable to display PC W-UXGA (1920x1200) signal at 60Hz

- It must be capable to display DVI-D with HDCP video signal (1080i25 and 720p50)

- It must have information position selectable

- In information area it must be possible to display Time code (embedded in connected HD/SD-SDI signal), audio level (of audio signals which are embedded in connected HD/SD-SDI signal)

- it must have brightness of at least 470cd/m²

- It must have contrast ratio at least 700:1

- Operating and service manual must be delivered with the equipment

| Option 2 | pieces |
| --- | --- |
| 1 | 20'' LCD monitors | 3 |

Audio equipment for DSNG van

Existing Audio Equipment, which will be delivered to the chosen bidder and must be installed in DSNG under items 1 to 8 below:

- Audio digital mixing console YAMAHA:

1piece--DM1000 V2

2piece--MY 16AE

1piece--SP 1000

1piece--MB 1000

Some inputs and outputs should be connected to patch panel and rear  termination panel ( as seen on audio schematic).

Audio monitoring of PFL-SOLO output  of mixing console is done on the  AMU1-BAS.

Program audio monitoring is done from embeded HD/SD signal of both destinations to satelite SAT1 and SAT2 on AMU2 -8HD.

- Audio monitoring TSL:

1piece--AMU2 8HD+ND

1piece--AMU1-BAS

GENELEC:

2pieces—8020 BPM

- GLENSOUND

1piece--GS-MP1005

1piece—GS-MP1005 Extra Interface

Communication between TV station, receiving the satelite  transmittion, and journalist  and guests is done via GSM phones. Equipment  should be connected to intercom matrix and audio mix console. Antennas for GSM communication must be mounted to the roof of the vehicle.

- AEQ

1piece—EAGLE AUDIOCODEC

Audio signal from codec should be connected to patch panel.  ISDN input should be connected to rear  termination panel to RJ45 connector.

- GHILMETTI

1piece--USF 2x32 AV 3/3 SA

140piece--GAS 323 LAC

20piece—313/60 D

- IFB MONITORING SENNHEISER

1piece—SR 2050

6piece—EK 2000 IEM AW-X

6piece—Telex headphone

Instructions from DSNG, broadcast journalist and guests come through intercom matrix to a wireless IFB system. Antennas for IFB system must be mounted to the roof of the vehicle.

- CLEARCOM  INTERCOM

1piece—ECLIPSE-PICO -36 port

1piece—IMF-3 FRAME

1piece—PSU-101 POWER SUPPLY

5piece—FOR 22 INTERFACE

1piece—V12LDX4-IP panel

1piece—110/340 microphone

1piece—AP-22 IFB panel

1piece—WCS 5.2 SOFTWARE

Inputs and outputs  which must have level  control contains FOR 22 interface.  Communication between  four wire equipment  is provide  through AP-22 IFB panel. Four wire equipment is connected to the intercom matrix via rear termination panel. One of the FOR22 should be connected to the patch panel.

- TELEX WIRELESS INTERCOM

1piece—BTR-700

2piece—TR-700

Intercom communication with any additional non-triax   camera, connected to EXT sources on rear termination panel  is done via wireless intercom system which  inputs and outputs  are connected to intercom matrix.

Equipment to be offered by the bidder and installed in DSNG

1.Digital clock with GPS control

Digital clock display with Hours/minutes/seconds,  case size cca 144x144x58mm , red colour display and GPS satellite time signal synchronization, recommended type model or equivalent  Wharton: 490A.02.R.S., 488 GPS

2.Rear Audio termination panels

Termination panels must be equipped with Neutik  XLR connectors and disignations strip

Recommended type model or equivalent: Canford: 2U -1x16 XLRM,  2U-1x16 XLRF

3. Rear Video termination panel

In the stowage area the rear video  termination panel with at least 22 BNC ,  2 triax Fisher, two fiber optics connectors with conversion loop from  fiber to  two  BNC connectors must be prepared.

4. web browser control of the equipment

All the equipment in the DSNG with web browser control capability must be controlled with web browser aplication on the PC notebook installed in the drawer in the rack.

- Engineering, Technical documentation

The bid must include the engineering and technical documentation with the schematics of the installed systems,at least the following:

- Electrical powering system

- RF installation

- Video installation

- Audio installation with communication

- Data- Ethernet installation, control, tally

- Drawings of the mechanical and electrical modifications on the vehicle

- Floor  plan of the vehicle with installation

- Longitudinal  an cross section of the vehicle

- Racks  layout

- Technical documentation must include the operational and service manuals in hard copy and  on electronic media for each machine, bought with this tender, detailed technical description of the systems in the vehicle, systems operating instructions, possibilities of round actions in case of failure, instructions for regular maintenance, instructions for fault finding, service manual for fault repairs

Four schematics are attached, which are the proposal, how the video/audio installation has to be wired. The schematics will have to be revised and finished by the chosen bidder. Changes can be accepted with the condition that every change has to be agreed by the tender authority. All wiring schematics of the bidder must  include the tag number of cable links between  the equipments, the same as there will be provided on the installed cables.

- Technical attachment no.1:  Video schematic

- Technical attachment no.2:  Audio schematic

- Technical attachment no.3:  3-rack  Lay-out

- Technical attachment no.4:  Audio and Communication  journalist-DSNG

- Technical attachment no.5:  DSNG Van floor plan

- Visiting , factory acceptance, commissioning of the vehicle at integrator location

The offer must include two visiting of the vehicle at integrator’s location:

- First visiting in the 1-day time duration must be in 30 days from the time of receiving the document proving the delivery of the vehicle to the integrator location, after the coach building, before the audio/ video equipment installation and cabling. The visiting must comprise the detailed inspection of the coach builder work done on the vehicle, the accordance with the tender technical requirements and the possibility of the corrections is required. The inspection and confirmation of the installation and wiring schematics will be done. The results of the inspection will be written and signed from both contracting parties.

- Second visiting in the time duration of 2 days at least must be after the installation and comprise the factory acceptance, testing of all the systems, installed electrical and electronic equipment and functionality. The DSNG van must transmit the TV signal from the installed camera over the satellite to RTVSLO Ljubljana and receive the back signal.

Testing of the communication equipment will be done. The bidder has to provide the microphone equipment for the testing.

All eventual incorrectness, ascertained at factory acceptance procedure, are to be eliminated by the Bidder within 14 days. After this deadline the procedure of the factory acceptance will be repeated if the experts of the Contract authority find it necessary.

The offer must include the travelling and accommodation expenses for the three experts of the Contracting authority   on first and second visiting at the integrator location. The costs are to be borne by the Bidder.

The results of the second visiting will be written and signed from both sides. The acceptance protocol will be written and signed from both contracting parties.

- Final acceptance and operational-maintenance training on the RTVSLO location

The bidder has to deliver the vehicle with installed equipment to the location of the Contracting Authority RTV Slovenija in Ljubljana.

- The quantity acceptance will be done in 5 working days after the delivery of the DSNG van with installed equipment to the location of RTVSLO in Ljubljana. With the quantitative acceptance the Contracting Authority will determine completeness of the vehicle regarding contract agreement.

- The final acceptance of the DSNG van must be completed by the Contracting Authority within twenty one (21) days after the date of successfully quantitative acceptance.

The Contracting Authority shall determine with the final acceptance whether the equipment is working according to the requested technical and functional requirements in tender documentation. At this final acceptance the representatives of the Bidder can be present.

All eventual incorrectness, ascertained at final acceptance procedure, are to be eliminated by the Bidder within 21 days, after this deadline the Contracting Authority may cash-in a performance guarantee, and the Bidder must submit a new Performance Guarantee.

It is understood that the final acceptance will be completed when all eventual incorrectness are eliminated. The incorrectness is to be specified in writing by the Contracting Authority.

The warranty time starts on the day of signing the final acceptance.

- The contracting authority require the operational-maintenance training for the 6-8  users of the DSNG van in duration of at least 2 days per 8 hours after the final acceptance on location of the Contracting  Authority.

The bidder had to cover all the expenses for the training (expenses for the literature, any cost connected to the training, accommodation, travel expenses for the lecturer).

The training must include the following:

- explanation of the operation of powering system in the vehicle,

- explanation of the operation of all stages of RF transmitting and receiving chain,

- explanation of adjustments, optimizing, measurements of individual stages, practical adjustments for optimal operation, tuning,  each participant must personally perform those settings,

- instructions and suggestions for error finding and re-launch of individual functions (each participant must personally perform those tasks),

- final examination and granting of a certificate for operational work, fault finding and simple faults repair on systems of DSNG van.

Education and related material must be in the Slovenian or English language.

The expenses for the operational-maintenance training must be included in the main offer.

The Contracting Authority reserves the right to reduce or increase the number of participants and/or days of schooling in terms of the number and complexity of the equipment.

The bidder must offer the price of additional day of training, which must not be included in the price of the main offer.

- References

The bidder must state in the bid the data of the DSNG vehicles, he has made in the period 2005 to now.

Minimal 4 reference DSNG vehicles are required; the bidder with less than 4 reference vehicles will be eliminated.

The bid has to include the photos of the reference vehicles  inside ( cabin and rear storage area) and outside, the list of installed equipment, contact data of the user of the reference DSNG van ( name, address, phone number, e-mail address, web page address), who will be prepared to answer to our questions about reference vehicle.

If  the tender commission estimated necessary, the inspection of the most comparable vehicle to the described in this tender documentation would be made in 14 days after the opening of the bids. The bidder must state the address of the location and contact details of the person to arrange the visit.

On the visit the commission will look at the following:

- Waterproof Tightness of the coach cuts must be 100%

- Cables passing the coach cuts must not have trace of  damage

- Efficient and user friendly air conditioning

- No rust on the coach 5 years after the vehicle accomplishment

- The cabine and rear storage area must be treated aesthetically with high quality materials, resistant to wear out

- Installation of RF , video and audio equipment and cables must be made with expert knowledge.

If the commission find out that the inspected reference DSNG van does not fullfill the requirements, the bid will be eliminated.

## LOT B

TRANSMITTING- RECEIVING EQUIPMENT

The bid under the lot B must include all items from the table: »Specification of the basic offer for the lot B: Transmitting-receiving equipment«. The price of each item must be given separately.

Optional offers 3,4 and 5 are obligatory and include equipment to be integrated into the vehicle.

In case the Contracting Authority decides for the purchase of one or more options already at the Decision on the award of a Contract, the same will be included in the basic Contract. In case the Contracting Authority decides for the purchase of optional offers later   (in the period of one year from the beginning of the Contract validity, subject to available financial resources and actual needs), the contractual parties shall conclude an Annex to the Contract JN-B0454.

In the case, that the Lot B and optional offers 3,4,5 won’t be bought with the chosen bidder of the Lot  A, the equipment described in the Lot B and optional offers 3,4,5 will be delivered to the chosen bidder of the  lot A for integration by the Contracting Authority.

### Specification of the basic offer for the LOT B: transmitting-receiving equipment:

| Specification of the basic offer for the LOT B | qty |
| --- | --- |
|  | Transmitting-receiving equipment |  |
| 1 | MPEG-2/4, 4:2:2/4:2:0 SD encoder/modulator, SW upgradeable on HD | 1 |
| 2 | MPEG-2/4 4:2:2/4:2:0 HD/SD,DVB-S2 receiver/demodulator | 1 |

Technical requirements for lot B:

Encoder/ modulator

- Integrated encoder/modulator ,MPEG-2 SD and MPEG-4 SD, 4:2:2 and 4:2:0, DVBS/DVB-S2, Q/8PSK software up-gradeable to HD, must ensure the broadcast contribution quality of the TV signal  in 1RU chassis with main and redundant power supply

- Integrazed encoder/modulator built in 1RU chassis

- main and redundant power   supply built in each chassis

- hot swappable encoder and modulator modul

- IP and ASI output

- MPEG-2 4:2:0 and 4:2:2(to MP@high level profile) encoding in SD and HD formats when  software HD upgrade option 5 installed

- MPEG-4-AVC 4:2:0 and 4:2:2 (to High422 profile) encoding in SD and HD formats with software HD upgrade option 5 installed

- Format support 1080i,720p,576i

- 10 bit coding

- SD/HD auto sensing input when  software HD upgrade option 5 installed

- Contribution quality bit rate 1Mbps to 80Mbps, when software upgrade option 5 installed

- Future support 1080p50

- AES/EBU audio inputs, Embedded audio on HD/SD SDI inputs and on separate AES/EBU audio connector, to 8 stereo pairs

- MPEG-1 Layer II audio coding

- Closed caption transport

- BISS scrambling

- DVB-S QPSK and DVB-S2 (QPSK,8PSK,16APSK) modulator integrated in the same chassis as encoder

- IF and L-band outputs

- Control via front panel (rotary control for fast item selection, key-pad for easy value insertion)

- High-resolution display and video/audio confidence monitoring on the chassis

- User management via web browser control and XML

- SNMP v1/v2/v3 for alarm traps

- Operating and service manual must be delivered with the equipment

Receiver/ Demodulator

- IRD receiver/demodulator in 1RU chassis with main and redundant power supply

- 4x L-band inputs with demodulation DVB-S QPSK and DVB-S2 QPSK/8PSK/16APSK

- IP input

- ASI input

- Automatic switch over to ASI input when primary input is lost

- BISS scrambling

- Decoding  MPEG-2 4:2:2 and 4:2:0 at HD and SD signal format

- Decoding MPEG-4-AVC 4:2:2 in 4:2:0 at HD and SD signal format

- Audio decoding and crossover possibilities:

- 6x MPEG-1 Layer 2 Decode

- 6x Dolby® Digital 2.0 decode and pass through

- 4x Dolby® Digital 5.1 pass-through

- 6x Dolby® Digital 5.1 downmix to 2.0 then decode

- 4x Dolby® E 5.1 pass-through

- VBI support (4:2:0 modes): WST, Inverted Teletext, EBU Teletext subtitles and non-subtitles, WSS, Video index, AFD Pass-through

- Operating and service manual must be delivered with the equipment

### OP3. Optional offer no. 3

| Option 3 – encoder/modulator | Qty |
| --- | --- |
| 1 | MPEG-2/4, 4:2:2/4:2:0 SD encoder/modulator, SW upgradeable on HD | 1 |

Technical requirements for option 3:

Encoder/ modulator

- Integrated encoder/modulator ,MPEG-2 SD and MPEG-4 SD, 4:2:2 and 4:2:0, DVBS/DVB-S2, Q/8PSK software up-gradeable to HD, must ensure the broadcast contribution quality of the TV signal  in 1RU chassis with main and redundant power supply

- Integrazed encoder/modulator built in 1RU chassis

- main and redundant power   supply built in each chassis

- hot swappable encoder and modulator modul

- IP and ASI output

- MPEG-2 4:2:0 and 4:2:2(to MP@high level profile) encoding in SD and HD formats when  software HD upgrade option 5 installed

- MPEG-4-AVC 4:2:0 and 4:2:2 (to High422 profile) encoding in SD and HD formats with software HD upgrade option 5 installed

- Format support 1080i,720p,576i

- 10 bit coding

- SD/HD auto sensing input when  software HD upgrade option 5 installed

- Contribution quality bit rate 1Mbps to 80Mbps, when software upgrade option 5 installed

- Future support 1080p50

- AES/EBU audio inputs, Embedded audio on HD/SD SDI inputs and on separate AES/EBU audio connector, to 8 stereo pairs

- MPEG-1 Layer II audio coding

- Closed caption transport

- BISS scrambling

- DVB-S QPSK and DVB-S2 (QPSK,8PSK,16APSK) modulator integrated in the same chassis as encoder

- IF and L-band outputs

- Control via front panel (rotary control for fast item selection, key-pad for easy value insertion)

- High-resolution display and video/audio confidence monitoring on the chassis

- User management via web browser control and XML

- SNMP v1/v2/v3 for alarm traps

### OP4. Optional offer no. 4

| Option 4 – receiver/demodulator | Qty |
| --- | --- |
| 1 | MPEG-2/4 4:2:2/4:2:0 HD/SD,DVB-S2 receiver/demodulator | 1 |

Technical requirements for option 4

Receiver/ Demodulator

- IRD receiver/demodulator in 1RU chassis with main and redundant power supply

- 4x L-band inputs with demodulation DVB-S QPSK and DVB-S2 QPSK/8PSK/16APSK

- IP input

- ASI input

- Automatic switch over to ASI input when primary input is lost

- BISS scrambling

- Decoding  MPEG-2 4:2:2 and 4:2:0 at HD and SD signal format

- Decoding MPEG-4-AVC 4:2:2 in 4:2:0 at HD and SD signal format

- Audio decoding and crossover possibilities:

- 6x MPEG-1 Layer 2 Decode

- 6x Dolby® Digital 2.0 decode and pass through

- 4x Dolby® Digital 5.1 pass-through

- 6x Dolby® Digital 5.1 downmix to 2.0 then decode

- 4x Dolby® E 5.1 pass-through

- VBI support (4:2:0 modes): WST, Inverted Teletext, EBU Teletext subtitles and non-subtitles, WSS, Video index, AFD Pass-through

### OP5. Optional offer no. 5

| Option 5 – encoder HD licence | qty |
| --- | --- |
| 1 | MPEG-2/4, 4:2:2/4:2:0 SD encoder/modulator under option3 SW upgrade (licence) to HD | 2 |

Option 5 includes the licence for upgrading the encoder from the main offer of lot B and from the option3. Licence will enable the encoding and modulation of HD SDI TV signals as follows:

- MPEG-4-AVC 4:2:0 and 4:2:2 (to High422 profile) encoding in HD and SD formats

- MPEG-2 4:2:0 and 4:2:2(to MP@high level profile) encoding in HD and SD formats

### Final acceptance of the transmitting-receiving equipment

Bidder shall supply the equipment under the lot B within six (6) weeks after the validity date of the Contract.

The quantitative acceptance will be done in the warehouse of RTV Slovenija, Čufarjeva Street 6, Ljubljana within three (3) working days after the equipment is delivered to the warehouse of RTV Slovenija.

With the quantitative acceptance the Contracting Authority will determine completeness of equipment regarding contract agreement.

The final acceptance of the delivered goods (equipment) must be completed by the Contracting Authority within seven (7) days after the date of quantitative acceptance.

The Contracting Authority shall determine with the final acceptance whether the equipment is working according to the requested technical and functional requirements in tender documentation. At this final acceptance the representatives of the Bidder can be present.

All eventual incorrectness, ascertained at final acceptance procedure, are to be eliminated by the Bidder within 21 days, after this delivery deadline the Contracting Authority may cash-in a performance guarantee.

It is understood that the final acceptance will be completed when all eventual incorrectness are eliminated. The incorrectness is to be specified in writing by the Contracting Authority.

The warranty time starts on the day of signing the final acceptance.

# BID DOCUMENTATION

## General conditions for making bid documentation

### Clarification to the tender documentation

The Bidder can demand clarifications to tender documentation in e-mail or written  form only, using the attached form, at the latest 6 days prior to the term for acceptance of bids, to the e-mail address: javna.narocila@rtvslo.si   or  fax no. + 386 1 475 2186. Questions, not asked on the prescribed form, will not be answered.

Questions and answers shall be published on web side: www.rtvslo.si/razpisi, on sub-page JAVNA NAROČILA - PUBLIC PROCUREMENT under the mark Javno naročilo JN-B0454.

### Language

Bids have to be made in Slovenian or in English language.

### Marking

Pages of bid documentation must be numbered and bound with string so it is not possible to add pages.

Data which will be righteously marked as confidential by the Bidder, will be used only for the purposes of this public tender and will not be accessible to anyone except persons which are included in this public tender. These data will not be read on public opening of the Bids nor will they be read afterwards. Persons, included in this public tender as well as the Contracting Authority will be responsible for protection of these data.

The Bidder can mark data as confidential only if they include personal data which are not included in other public register nor otherwise acceptable to public. The Bidder can also mark as confidential business information which are marked as confidential either with regulations or internal acts of the Bidder.

The Contracting Authority will treat as confidential all data in bid documentation which will be in right upper corner marked as "CONFIDENTIAL" with large capital letters. Under this inscription there should be signature of the Bidder's official representative or authorized person. If only part of the document is confidential, the confidential part should be underlined with red colour and in the same line marked "CONFIDENTIAL" at the right edge.

The Contracting Authority will not be responsible for confidentiality of the data if these data are not marked as stated above.

The Contracting Authority will summon the Bidder to withdraw the confidential mark if the data is unjustified marked as confidential. The confidential mark can be withdrawn by the Bidder's official representative or authorized person writing "CANCELLATION" above the confidential mark. He must also write time and date of this cancellation and sign it.

In the case of a Bidder not withdrawing the confidential mark in the time, determined by Contracting Authority, the Contracting Authority will reject the complete bid.

### Contents of a bid

The Bidders can submit their bids for the equipment, required in the tender documentation:

- for all the required equipment

- for equipment according to single Lot, wherein all the equipment, stated in the single Lot, has to be offered.

### Alternative bids and variant bids

Alternative bids and variant bids are not allowed.

### Validity of the bids

Bids must be valid till 12 September, 2011, otherwise they will be rejected. In exceptional circumstances the Contracting Authority can demand from the Bidder to extend the validity of the bid for a certain period of time. The Contracting Authority's demand and the Bidder's replies must be in written form. The Bidder can refuse the Contracting Authority's demand. In case the Bidder complies with the demand, the Contracting Authority shall ask for the bid extension and eventually for the extension of the validity of the Warranty for the seriousness of the bid. All other conditions of the bid shall remain the same.

## Documents in the bids

The bid documentation must contain the following documents, sorted in the following order:

### Data on Bidder and Bid

### Contents of the bid documentation

### Form »Declaration on acceptance of the public tender conditions«

### Form of an OFFER that has to contain:

Prices:

- Prices must be expressed in EUR, on DDP Ljubljana basis, delivered to the location of the Contracting Authority in Ljubljana (in accord. with INCOTERMS 2000); without VAT.

Offered discounts must be shown separately.

The prices must be fixed for the period of the Contract duration.

The Bidder has to offer also the values of the optional offers, according to the requirements in items 3.2 and 3.3.

The Contracting Authority shall not present bank warranty or any other instrument for insurance of the retained payments.

Payment conditions for the LOT A

- After the submission of the evidence on the purchase of the vehicle for the Contracting Authority, the Bidder shall issue the invoice for the first situation (I.) in the amount of 20% of the contractual value. The Contracting Authority will pay the amount of the first situation within 30 days after the acceptance protocol has been signed by the Bidder and the Contracting Authority, by which the Contracting Authority will acknowledge receipt of proof that the Bidder bought the appropriate vehicle for the Contracting Authority.

- After the second visit, which includes technical acceptance, inspection and launch of DSNG vehicle, which must be validated with the acceptance protocol, the Bidder shall issue an invoice for the second situation (II.) in the amount of 60% of the contractual value. The Contracting Authority will pay the amount of the second situation within 30 days after the acceptance protocol of a successful technical acceptance has been signed by the Bidder and the Contracting Authority. An invoice without the acceptance protocol will be rejected.

- After the final acceptance of the vehicle has been successfully carried out, the Bidder shall issue an invoce for the third situation (III.) in the amount of 20% of the contractual value. The Contracting Authority will pay the amount of the third situation within 30 days after the final acceptance of the vehicle with integrated additional equipment has been successfully carried out and after the acceptance protocol has been signed by the Contacting Authority.

Payment conditions for the LOT B

- 100 % within 30 days after the final acceptance of the goods on location of the Contracting Authority  (in accordance with the requirements in item 3.3.5 of Tender Documentation)

Delivery date:

The Contracting Authority requires delivery date:

- LOT A - at the latest within 6 months after the beginning of the Contract validity

- LOT B - at the latest within 6 weeks after the beginning of the Contract validity

Optional offers:

The Bidder has to offer separately from the basic offer also the values of the optional offers, according to the requirements in items 3.2 and 3.3.

All the Contracting Authority’s technical and quantitative requirements for optional offers are in the tender documentation text marked with blue color and are in the technical specifications reasonably added to the end of textual statements of the each connected particular basic requirements.

All optional offers must be obligatory.

In case the Contracting Authority decides for the purchase of one or more options already at the Decision on the award of a Contract, the same will be included in the basic Contract. In case the Contracting Authority decides for the purchase of optional offers later   (in the period of one year from the beginning of the Contract validity, subject to available financial resources and actual needs), the contractual parties shall conclude an Annex to the Contract JN-B0454.

The value of optional offers is not included in the anticipated value of public tender JN-B0454.

### Pro forma Invoice

### Bidder's “Statement on criminal offences from the first and the second paragraph of Article 42 of the Public Procurement Act (ZJN-2C)” – for a legal entity

A Bidder with the registered office in the Republic of Slovenia must submit the signed statement. The Bidder may submit official documents as evidence of meeting the conditions specified in this statement. Such evidence must not be dated more than 30 days prior to the date set for the submission of bids.

Pursuant to the fifth paragraph of Article 42 of ZJN-2C the Bidder with the registered office in the Republic of Slovenia may, instead of providing evidence, state in the bid the relevant record and the competent national body, local community body or a person with public authority from whom such official data may be obtained by the Contracting Authority itself. In such case, the Bidder must attach to the bid the authorisation for the Contracting Authority to obtain the relevant evidence itself.

A Bidder with the registered office outside the Republic of Slovenia must submit the signed statement. The Bidder must also submit official documents from its country as evidence of meeting the conditions specified in this statement. Such evidence must not be dated more than 30 days prior to the date set for the submission of bids.

If the country of the Bidder with the registered office outside the Republic of Slovenia does not issue such documents, the Contracting Authority may accept a sworn statement of witnesses or a sworn statement of the Bidder instead of official documents from its country. In such case, the Bidder must make the above statement before a judicial or administrative body, Notary Public or the competent body for professional or economic operators in the country of their registered office.

### Bidder's “Statement on criminal offences from the first and the second paragraph of Article 42 of the Public Procurement Act (ZJN-2C)” – for a legal representative

If the Bidder has more than one legal representative, he must enclose “Bidder's Statement on criminal offences from the first and the second paragraph of Article 42 of the Public Procurement Act (ZJN-2C)” for each of them.

A Bidder with the registered office in the Republic of Slovenia must submit the signed statement. The Bidder may submit official documents as evidence of meeting the conditions specified in this statement. Such evidence must not be dated more than 30 days prior to the date set for the submission of bids.

Pursuant to the fifth paragraph of Article 42 of ZJN-2C the Bidder with the registered office in the Republic of Slovenia may, instead of providing evidence, state in the bid the relevant record and the competent national body, local community body or a person with public authority from whom such official data may be obtained by the Contracting Authority itself. In such case, the Bidder must attach to the bid the authorisation for the Contracting Authority to obtain the relevant evidence itself.

A Bidder with the registered office outside the Republic of Slovenia must submit the signed statement.

The Bidder must also submit official documents from its country as evidence of meeting the conditions specified in this statement. Such evidence must not be dated more than 30 days prior to the date set for the submission of bids.

If the country of the Bidder with the registered office outside the Republic of Slovenia does not issue such documents, the Contracting Authority may accept a sworn statement of witnesses or a sworn statement of the Bidder instead of official documents from its country. In such case, the Bidder must make the above statement before a judicial or administrative body, Notary Public or the competent body for professional or economic operators in the country of their registered office.

### Form “Statement under the fourth paragraph of article 42 of the ZJN-2C”

### Form “Bidder’s statements, given under criminal and material liability”

### Bank Certificate of solvency

The Bidder must enclose Bank Certificate of solvency, showing the Bidder’s account has not been blocked within the last six months. On the date of opening of the bids, this Certificate must not be older than one month.

If the Bidder has several accounts, he must enclose Bank Certificate of solvency for all accounts.

The document (under item 4.2.10) may also be a photocopy. In such case the Bidder has to inscribe on each photocopied page, that he confirms the truthfulness of the stated data and sign and stamp this statement on  each photocopied page. In case the Contracting Authority subsequently requests the original evidence, the Bidder shall present the same for verification.

### Warranty conditions of the Bidder

Warranty conditions for the Lot A:

The warranty period for the vehicle in the Lot A:

- 24 months 			for  units and mechanisms with 100.000 km mileage limit

- 5 years				for the paint on the vehicle

- 8 years				for bodywork anti-perforation

The warranty period for the equipment offered in the Bid for the Lot A and integrated in the vehicle must be equal or longer than the warranty period offered from the direct manufacturers of offered equipment , but at least two (2) years from the successful final acceptance of the vehicle with integrated equipment under lot A.

The Bidder must enclose his own statement with the detailed information on the maintenance of equipment in warranty period, according to the requirements, stated in the chapter “Warranty conditions” in the TECHNICAL PART of Tender documentation, from which must be evident:

- The address, phone and e-mail of the service expert who advices the RTVSLO service expert during the warranty period

- the address of the European service for bidden equipment, contact person, phone and fax number

- response time and the time period when the error will be eliminated or time period when the Bidder will ensure the replacement equipment.

The Bidder in his statement must ensure:

- For the warranty period: the dispatch of the replacement module by express courier service within 24 hours  (within the  working days),  from the receipt of the Contract Authority’s report by fax or e-mail. The Contracting Authority will return the defective module after receipt of the replacement one.

The Bidder must ensure that all the software upgrades for the offered technological equipment, installed in the DSNG van, will be free of charge for the Contracting Authority within the warranty period, except for the equipment delivered for integration from the Contracting Authority.

- For the after warranty period: the dispatch of the replacement module by express courier service within 48 hours  (within the  working days),  from the receipt of the Contract Authority’s report by fax or e-mail. The Contracting Authority will return the defective module after receipt of the replacement one and will pay it within 30 days after receipt of the invoice.

Warranty conditions for the Lot B:

The warranty period for the equipment offered in the Bid for the Lot B must be equal or longer than the warranty period offered from the direct manufacturers of offered equipment , but at least two (2) years from the successful final acceptance of the  equipment under lot B.

The Bidder must enclose his own statement with the detailed information on the maintenance of equipment in warranty period, according to the requirements, stated in the chapter “Warranty conditions” in the TECHNICAL PART of Tender documentation, from which must be evident:

- The address, phone and e-mail of the service expert who advices the RTVSLO service expert during the warranty period

- the address of the European service for bidden equipment, contact person, phone and fax number

- response time and the time period when the error will be eliminated or time period when the Bidder will ensure the replacement equipment.

The Bidder in his statement must ensure:

- For the warranty period: the dispatch of the replacement module by express courier service within 24 hours  (within the  working days),  from the receipt of the Contract Authority’s report by fax or e-mail. The Contracting Authority will return the defective module after receipt of the replacement one.

- For the after warranty period: the dispatch of the replacement module by express courier service within 48 hours  (within the  working days),  from the receipt of the Contract Authority’s report by fax or e-mail. The Contracting Authority will return the defective module after receipt of the replacement one and will pay it within 30 days after receipt of the invoice.

### Declaration of the Bidder regarding the spare parts

LOT A:

The Bidder must enclose his own statement regarding providing the spare parts for the offered technological equipment integrated into the DSNG vehicle and for the DSNG vehicle itself, for a period of at least seven (7) years after final acceptance.

LOT B:

The Bidder must enclose his own statement regarding providing the spare parts for the offered technological equipment for a  period of at least five (5) years after final acceptance.

### Declaration of the Bidder - all the offered equipment is factory-new

- Declaration of the Bidder for LOT A that the vehicle with integrated additional equipment purchased under this Public Tender is factory new.

- Declaration of the Bidder for LOT B that all equipment is factory new.

### Declaration of the Bidder regarding the software upgrades

### Statement of the manufacturer or principal

In case the Bidder is not also the manufacturer of the equipment, the mentioned statements are to be enclosed:

LOT A:

- Generator

- Air conditioning system

- Antenna system

LOT B:

- Transmitting – receiving equipment

If the Bidder encloses the statement of the principal, he has to enclose also the copy of the Contract between the principal and the manufacturer of the equipment, showing the principal has full access to the spare parts i.e. replacement equipment for all offered equipment.

### Sample of the Contract

Sample of the Contract, wherein each page is to be initialled and stamped by the Bidder's official representative or authorized person. Each article in the Contract is written first in Slovenian and then in English language. In case of any doubt or misunderstanding, the Slovenian version should therefore be considered final.

### Guarantee for the seriousness of the bid

The guarantee for the seriousness of the bid (issued by Bank or Insurance Company), irrevocable, unconditional, payable at first call, valid till 12 September, 2011:

- For LOT A in the value EUR 2.200.

- For LOT B the guarantee is not required.

### Declaration, stating the Bidder shall provide a Performance guarantee (for both lots)

### References

- LOT A:

The Bidder must enclose four (4) references according to requires in item 11, chapter 3.2.

- For LOT B references are not required.

### Technical documentation

The Bidder must enclose all relevant documentation, required in chapter 3 wherein it must be unambiguously evident that the bidden equipment fulfils all the technical requirements.

# CONTRACT AWARD CRITERIA

The criterion for the evaluation of the bids, that will fulfil all the conditions and requirements from this tender documentation and will be technically entirely corresponding to all conditions and technical specifications, is PRICE. The Bidder, whose bid reaches maximal number of points at each Lot, according to the below mentioned criteria, is going to be selected.

## CONTRACT AWARD CRITERIA FOR LOT A

The Contracting Authority will for the purposes of the evaluation add the values of basic and all required optional offers. The Bid with the lowest total value will at the evaluation receive 100 points, the remaining Bids will receive less points, expressed as percentage to the Bid with the lowest price, according to the following formula:

the sum of the estimated basic offer and all optional offers

( 2 -   --------	----------------------------------------------------------------------  )   	x   100

the sum of the  lowest basic offer and all optional offers

The calculation will be done on two decimal places. The bid can be appraised by 0 points at the minimum.

## CONTRACT AWARD CRITERIA FOR LOT B

The Contracting Authority will for the purposes of the evaluation add the values of basic and all required optional offers. The Bid with the lowest total value will at the evaluation receive 100 points, the remaining Bids will receive less points, expressed as percentage to the Bid with the lowest price, according to the following formula:

the sum of the estimated basic offer and all optional offers

( 2 -   --------	----------------------------------------------------------------------  )   	x   100

the sum of the  lowest basic offer and all optional offers

The calculation will be done on two decimal places. The bid can be appraised by 0 points at the minimum.

## TWO BIDS WITH EQUAL BEST EVALUATION RESULT

In case two or more bids have at the end of the evaluation equal maximum number of points, the Contracting Authority shall choose the bid that offers lower price of basic offer. Should the bid can not be chosen anyway, the next measure is lower price of optional offer.

# REVIEW CLAIM

## Legal base and terms for submission

Pursuant to the Act on the Review of Public Procurement Procedures (ZRPJN-UPB4, Official Gazette of the Republic of Slovenia No. 26/2007, ZRPJN-E, Official Gazette of the Republic of Slovenia No. 53/2007) the review claim may be submitted by any individual who showed or shows interest in the award of Contract and has suffered or could suffer damage due to the act of the Contracting Authority. The review claim may be submitted in all phases of public Contract award procedure and against any activity of the Contracting Authority unless otherwise provided by the law regulating the award of public Contract and the Act on the Review of the Public Procurement Procedures. After the Contract has been awarded, the term for submitting a review claim shall be ten days following the receipt of a Decision on the Award of a Contract.

The review of the Public Procurement Procedures shall be carried out according to the Act on the Review of Public Procurement Procedures, while the provisions related to the procedure of the Legal Procedure Act shall only apply unless otherwise provided by the Act on the review of the Public Procurement procedures.

## Method of submitting the review claim

The review claim must be explained. The Applicant shall forward the review claim to the Contracting Authority in two copies. Slovenian Ministry in charge of finance shall be notified by one copy of the review claim. The review claim shall be sent to the Contracting Authority through registered mail with A.R. (advice of receipt), or electronically (if the signature is verified).

The Applicant shall state the following data on the review claim:

- the Applicant of the review claim and the contact person;

- the name of the Contracting Authority;

- the public procurement (i.e. tender) and the notification on awarding the Contract or recognizing the qualifications;

- infringements;

- facts and evidences proving the infringements;

- evidence on the payment of a tax in the value of  EUR 5.000,00; made to the adequate account at the Ministry in charge of finance. The account No.: 01100-1000358802.

The Contracting Authority shall reject  all incorrect claims and claims not submitted within the above stated period.

# FORMS

The enclosed forms must be completed and attached to the Bid.

## DATA ON BIDDER AND BID

FOR PUBLIC TENDER – JN-B0454

Purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting

(by lots).

To be completed by a Bidder. Valid data that are accessible in public and according to the regulations related to a status and legal form are obligatory. The Contracting Authority shall examine some data through electronic media available.

| BID NO.: |  |
| --- | --- |
| COMPANY NAME / NAME OF THE BIDDER: |  |
| LEGAL STATUS OF THE BIDDER: |  |
| ADDRESS OF THE BIDDER: |  |
| NUMBER OF (BUSINESS) ACCOUNT - IBAN, SWIFT: |  |
| BANK’S ADDRESS: |  |
| CONTACT PERSON RESPONSIBLE FOR A BID: |  |
| E-MAIL OF CONTACT PERSON, PHONE AND FAX: |  |
| ID VAT NO. OF A BIDDER.: |  |
| COMPANY REGISTRATION NO. OF A BIDDER.: |  |
| PERSON RESPONSIBLE FOR SIGNING A CONTRACT: |  |
| FUNCTION OF PERSON RESPONSIBLE FOR SIGNING A CONTRACT: |  |

Validity of the bid: ………………………………….(at least till 12 September, 2011)

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

## Declaration of Bidder’s acceptance of Public Procurement conditions

JN-B0454

The Bidder:

- Title and name of the Bidder: ………………………………………………………………

-  Address: .....................................................................................................................

-  Bidder's official representative or authorized person: …………………………………

We herewith declare, that we accept all the conditions, required in the tender documentation for the submission of our bid on the published tender for the purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting (by lots).

(please encircle)

- LOT A:  Purchase and integration of the DSNG van

- LOT B:  Transmitting-receiving equipment

We declare, that all data, given in our bid documentation are truthful, and that all the enclosed document photocopies equal to the originals. For given data, their truthfulness and suitability of photocopies we assume full responsibility.

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

.

## Form OFFER – LOT A

FOR PUBLIC TENDER JN-B0454

Purchase and integration of the DSNG van – BASIC OFFER

| No. | Description | qty | Value in EUR without VAT |
| --- | --- | --- | --- |
| 01 | Vehicle Panel Van, 5t | 1 |  |
| 02 | Vehicle coachwork | 1 |  |
| 03 | Electrical system | 1 |  |
| 3A | Generator | 1 |  |
| 3B | UPS system for redund.powering of both RF chains for 10 minutes | 1 |  |
| 04 | Air conditioning system | 1 |  |
| 05 | Antenna system | 1 |  |
| 06 | Installation of the transmitting-receiving equipment | 1 |  |
| 07 | Video/audio installation | 1 |  |
| 08 | Engineering, technical documentation | 1 |  |
| 09 | Visiting, factory acceptance, commissioning of the vehicle at integrator location | 1 |  |
| 10 | Final acceptance , user training on location of the Contracting Authority | 1 |  |
| 11 | Price of vehicles and equipment, according to the requirements in item 3.2.1 of tender documentation for the basic offer |  |
| 12 | Allowed discounts |  |
| 13 | TOTAL NET - DDP Ljubljana, delivered on location of the Contracting Authority RTV Slovenija, Ljubljana (accor. to INCOTERMS 2000); without VAT |  |

Price of additional day of school, which is not taken into account in basic offer;……………………..

Payment conditions:

- After the submission of the evidence on the purchase of the vehicle for the Contracting Authority, the Bidder shall issue the invoice for the first situation (I.) in the amount of 20% of the contractual value. The Contracting Authority will pay the amount of the first situation within 30 days after the acceptance protocol  has been signed by the Bidder and the Contracting Authority, by which the Contracting Authority will acknowledge receipt of proof that the Bidder bought the appropriate vehicle for the Contracting Authority.

- After the second visit, which includes technical acceptance, inspection and launch of DSNG vehicle, which must be validated with the acceptance protocol, the Bidder shall issue an invoice for the second situation (II.) in the amount of 60% of the contractual value. The Contracting Authority will pay the amount of the second situation within 30 days after the acceptance protocol of a successful technical acceptance has been signed by the Bidder and the Contracting Authority. An invoice without the acceptance protocol will be rejected.

- After the final acceptance of the vehicle has been successfully carried out, the Bidder shall issue an invoice for the third situation (III.) in the amount of 20% of the contractual value. The Contracting Authority will pay the amount of the third situation within 30 days after the final acceptance of the vehicle with integrated additional equipment has been successfully carried out and after the acceptance protocol has been signed by the Contacting Authority.

The Contracting Authority shall not present bank guarantee or any other instrument for insurance of the retained payments.

Delivery date:…………………………………..

Warranty:………………………………………...

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

## Form OFFER – LOT A

FOR PUBLIC TENDER JN-B0454

Purchase and integration of the DSNG van – OPTIONAL OFFER no.1 (item 3.2.2/OP1)

| Item | Description: | Value in EUR without VAT | qty | Total in EUR Without VAT |
| --- | --- | --- | --- | --- |
| 01 | 19" Rack Frame for 10 CardModules with fan front cover + Primary PSU+redundant PS |  | 2 |  |
| 02 | 1,5G 1>8 Wide Band Analog Video / Sync Distribution Amplifier |  | 2 |  |
| 03 | 3G/HD/SD 1>8 SDI Distribution Amplifier |  | 2 |  |
| 04 | 3G/HD/SD 16 Channel Embedder or De-embedder (selected an embeded function) - SubD balanced |  | 2 |  |
| 05 | 3G/HD/SD 16 Channel Embedder or De-embedder (selected a deembeder function)) - SubD balanced |  | 2 |  |
| 06 | SDTV Analog and Digital multifunction Processor (PAL-SDI conv.,emb,FS) |  | 2 |  |
| 07 | 1,5G SD/HD Monitoring Down converter with Analog and Digital Audio / Video Outputs |  | 2 |  |
| 08 | HD/SD SDI and AES Test Signal Generator with two test outputs, static and dynamic patterns, EBU A/V sync pattern for transmition alive, audio lip sync pattern |  | 1 |  |
| 09 | Price of offered Option 1 Modular equipment According to the requirements in chapter 3 – item 3.2.2 OP 1 |  |
| 10 | Allowed discounts |  |
| 11 | TOTAL NET - DDP Ljubljana, delivered on location of the Contracting Authority RTV Slovenija, Ljubljana (accor. to INCOTERMS 2000); without VAT |  |

The value of this option is not included in the anticipated value of public tender JN-B0454.

In case the Contracting Authority decides for the purchase of this option already at the Decision on the award of a Contract, the same will be included in the basic Contract. In case the Contracting Authority decides for the purchase of this option later (in the period up to one year from the beginning of the Contract validity, subject to available financial resources and actual needs), the contractual parties shall conclude an Annex to the Contract JN-B0454.

Payment conditions:

- 100 % - within 30 days after the final acceptance on location of the Contracting Authority

The Contracting Authority shall not present bank guarantee or any other instrument for insurance of the retained payments.

Delivery date:…………………………………………

Warranty:………………………………………………

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

## Form OFFER – LOT A

FOR PUBLIC TENDER JN-B0454

Purchase and integration of the DSNG van – OPTIONAL OFFER no.2 (item 3.2.3/OP2)

| Item | Description | qty | Value in EUR without DDV |
| --- | --- | --- | --- |
| 01 | Price of offered Option 2 20'' LCD monitors according to the requirements in chapter 3 – item 3.2.3 OP2 | 3 |  |
| 02 | Allowed discounts |  |  |
| 03 | TOTAL NET - DDP Ljubljana, delivered on location of the Contracting Authority RTV Slovenija, Ljubljana (accor. to INCOTERMS 2000); without VAT |  |

The value of this option is not included in the anticipated value of public tender JN-B0454.

In case the Contracting Authority decides for the purchase of this option already at the Decision on the award of a Contract, the same will be included in the basic Contract. In case the Contracting Authority decides for the purchase of this option later (in the period up to one year from the beginning of the Contract validity, subject to available financial resources and actual needs), the contractual parties shall conclude an Annex to the Contract JN-B0454.

Payment conditions:

- 100 % - within 30 days after the final acceptance on location of the Contracting Authority

The Contracting Authority shall not present bank guarantee or any other instrument for insurance of the retained payments.

Delivery date:………………………………………

Warranty:……………………………………………

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

## Form OFFER – LOT B

FOR PUBLIC TENDER JN-B0454

Transmitting-receiving equipment – BASIC OFFER

| Item | Description: | qty | Value in EUR without DDV |
| --- | --- | --- | --- |
| 01 | MPEG-2/4, 4:2:2/4:2:0 SD encoder/modulator, SW upgradeable on HD | 1 |  |
| 02 | MPEG-2/4 4:2:2/4:2:0 HD/SD,DVB-S2 receiver/demodulator | 1 |  |
| 03 | Allowed discount |  |
| 04 | S TOTAL NET - DDP Ljubljana, delivered on location of the Contracting Authority RTV Slovenija, Ljubljana (accor. to INCOTERMS 2000); without VAT |  |

Payment conditions:

- 100 % - within 30 days after the final acceptance on location of the Contracting Authority

The Contracting Authority shall not present bank guarantee or any other instrument for insurance of the retained payments.

Delivery date:………………………………………

Warranty:……………………………………………

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

## Form OFFER – LOT B

FOR PUBLIC TENDER JN-B0454

Transmitting-receiving equipment – OPTIONAL OFFER no. 3 (ITEM 3.3.2/OP3)

| Item | Description | qty | Value in without DDV |
| --- | --- | --- | --- |
| 01 | Price of offered Option 3 MPEG-2/4, 4:2:2/4:2:0 SD encoder/modulator, SW upgradeable on HD according to the requirements in chapter 3 – item 3.3.2 /OP3 | 1 |  |
| 02 | Allowed discount |  |  |
| 03 | S TOTAL NET - DDP Ljubljana, delivered on location of the Contracting Authority RTV Slovenija, Ljubljana (accor. to INCOTERMS 2000); without VAT |  |

The value of this option is not included in the anticipated value of public tender JN-B0454.

In case the Contracting Authority decides for the purchase of this option already at the Decision on the award of a Contract, the same will be included in the basic Contract. In case the Contracting Authority decides for the purchase of this option later (in the period up to one year from the beginning of the Contract validity, subject to available financial resources and actual needs), the contractual parties shall conclude an Annex to the Contract JN-B0454.

Payment conditions:

- 100 % - within 30 days after the final acceptance on location of the Contracting Authority

The Contracting Authority shall not present bank guarantee or any other instrument for insurance of the retained payments.

Delivery date:………………………………………

Warranty:……………………………………………

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

## Form OFFER – LOT B

FOR PUBLIC TENDER JN-B0454

Transmitting-receiving equipment – OPTIONAL OFFER no. 4 (ITEM 3.3.3/OP4)

| Item | Description | qty | Value in without DDV |
| --- | --- | --- | --- |
| 01 | Price of offered Option 4 MPEG-2/4 4:2:2/4:2:0 HD/SD,DVB-S2 receiver/demodulator according to the requirements in chapter 3 – item 3.3.3/OP4 | 1 |  |
| 02 | Allowed discount |  |  |
| 03 | S TOTAL NET - DDP Ljubljana, delivered on location of the Contracting Authority RTV Slovenija, Ljubljana (accor. to INCOTERMS 2000); without VAT |  |

The value of this option is not included in the anticipated value of public tender JN-B0454.

In case the Contracting Authority decides for the purchase of this option already at the Decision on the award of a Contract, the same will be included in the basic Contract. In case the Contracting Authority decides for the purchase of this option later (in the period up to one year from the beginning of the Contract validity, subject to available financial resources and actual needs), the contractual parties shall conclude an Annex to the Contract JN-B0454.

Payment conditions:

- 100 % - within 30 days after the final acceptance on location of the Contracting Authority

The Contracting Authority shall not present bank guarantee or any other instrument for insurance of the retained payments.

Delivery date:………………………………………

Warranty:……………………………………………

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

## Form OFFER – LOT B

FOR PUBLIC TENDER JN-B0454

Transmitting-receiving equipment – OPTIONAL OFFER no. 5 (ITEM 3.3.4/OP5)

| Item | Description | qty | Value in without DDV |
| --- | --- | --- | --- |
| 01 | Price of offered Option 5 MPEG-2/4 4:2:2/4:2:0 SD encoder/modulator , SW upgrade (licence) to HD according to the requirements in chapter 3 – item 3.3.4/OP5 | 1 |  |
| 02 | Allowed discount |  |  |
| 03 | S TOTAL NET - DDP Ljubljana, delivered on location of the Contracting Authority RTV Slovenija, Ljubljana (accor. to INCOTERMS 2000); without VAT |  |

The value of this option is not included in the anticipated value of public tender JN-B0454.

In case the Contracting Authority decides for the purchase of this option already at the Decision on the award of a Contract, the same will be included in the basic Contract. In case the Contracting Authority decides for the purchase of this option later (in the period up to one year from the beginning of the Contract validity, subject to available financial resources and actual needs), the contractual parties shall conclude an Annex to the Contract JN-B0454.

Payment conditions:

- 100 % - within 30 days after the final acceptance on location of the Contracting Authority

The Contracting Authority shall not present bank guarantee or any other instrument for insurance of the retained payments.

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

## Proforma Invoice

FOR PUBLIC TENDER JN-B0454

The Bidder must enclose the detailed breakdown of prices for each item of the offer (for each bidden Lot separately, and also for basic and for each optional offers).

The allowed discount must be shown separately.

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

Bidder: ………………………………………………………………

Address: .............................................................................

## Statement on criminal offences from the first and the second paragraph of Article 42 of the Public Procurement Act (ZJN-2C)

FOR A LEGAL ENTITY

FOR PUBLIC TENDER JN-B0454

We hereby declare under criminal and material liability that against our Company there have not been issued  legally binding judgements for criminal offences that are defined in Penal Code (Official Gazette of the Republic of Slovenia, no. 55/08, 66/08 – correct. 39/09):

- crime gathering;

- forbidden receiving of gifts, forbidden giving of gifts, giving bribes, receiving of gifts for unlawful interventions and giving  gifts for unlawful interventions,

- fraud,  business fraud, imposture at gaining loan or benefits and denial of financial obligations,

- money laundering.

Furthermore, we declare under criminal and material liability that against our Company there have not been issued legally binding judgements for fraud against financial interests of European Communities (according to the 1. Art. of Convention on the protection of the European Communities’ financial interests).

As evidence that we have not been finally convicted of any indicated criminal offences,

(Circle as appropriate)

- We attach the certificate of no convictions from the official record.

- Our country does not issue such documents. Therefore the subject statement has been made and signed before: (name one of the following competent bodies: a judicial or administrative body, Notary Public or the competent body for professional or economic operators in the country): ...............................................................................................................................................

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

Place and date: 			Stamp:			    Signature of the competent body

........................................					.........................................................

Bidder's LEGAL REPRESENTATIVE:

Name and surname: .................................................

## Statement on criminal offences from the first and the second paragraph of Article 42 of the Public Procurement Act (ZJN-2C)

FOR A LEGAL REPRESENTATIVE

FOR PUBLIC TENDER JN-B0454

I, the undersigned, hereby declare under criminal and material liability that against me there have not been issued  legally binding judgements for criminal offences that are defined in Penal Code (Official Gazette of the Republic of Slovenia, no. 55/08, 66/08 – correct. in 39/09):

- crime gathering;

- taking bribes at elections, forbidden receiving of gifts, forbidden giving of gifts, taking bribes, giving bribes, receipt of gifts for unlawful interventions and giving gifts for unlawful interventions,

- fraud,  business fraud, imposture at gaining loan or benefits and denial of financial obligations,

- money laundering.

Furthermore, I declare under criminal and material liability that against me there have not been issued legally binding judgements for fraud against financial interests of European Communities (according to the 1. Art. of Convention on the protection of the European Communities’ financial interests).

As evidence that I have not been finally convicted of any indicated criminal offences,

(Circle as appropriate)

- I attach the certificate of no convictions from the official record.

- Our country does not issue such documents. Therefore the subject statement has been made and signed before: (name one of the following competent bodies: a judicial or administrative body, Notary Public or the competent body for professional or economic operators in the country): ....................................................................................................................................................

Place and date: 					         Signature of Bidder’s legal representative

........................................					.........................................................

Place and date: 			Stamp:			    Signature of the competent body

........................................					.........................................................

Bidder: ………………………………………………………………

Address: .............................................................................

## STATEMENT UNDER THE FOURTH PARAGRAPH OF ARTICLE 42 OF THE ZJN-2C

FOR PUBLIC TENDER JN-B0454

Under criminal and material liability we hereby declare that:

- our company is not undergoing bankruptcy proceedings;

- a member of our management or supervisory body or a representative as stipulated by the act regulating financial operations, insolvency proceedings and compulsory winding-up, has not been, in the period of two years prior to the expiry of the deadline for submitting the bids in the public tender procedure, a partner with a holding above 25 percent or a shareholder with a holding above 25 percent or a member of the management or supervisory body or a representative of such operator against which bankruptcy proceedings, compulsory settlement or compulsory winding-up proceedings have been initiated;

- on the day of expiry of the deadline for submitting bids, we have no outstanding non-paid obligations relating to the payment of social security contributions in accordance with the legal provisions of the country of our registered office or with those of the country of the Contracting Authority;

- on the day of expiry of the deadline for submitting bids, we have no outstanding non-paid obligations relating to the payment of taxes in accordance with the legal provisions of the country of our registered office or with those of the country of the Contracting Authority.

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

Bidder: ………………………………………………………………

Address: ......................................................................................

## Bidder's Statements given under criminal and material liability

FOR PUBLIC TENDER JN-B0454

- We hereby declare under criminal and material liability that we are registered by the competent entity of the state and have valid extract from judicial or other records, as well as all the necessary permits from the body competent for the activity which is the subject of this public tender.

- We hereby declare under criminal and material liability that no proposal for initiating bankruptcy proceedings, compulsory settlement or compulsory winding-up proceedings against our company has been submitted and that we are not currently undergoing compulsory settlement or compulsory winding-up proceedings. Our business is not, for any other reasons, managed by a court and we have not discontinued our business activity or found ourselves in a similar situation.

- We hereby declare under criminal and material liability that our firm is reliable, capable of managing a business, has sufficient technical capabilities, experiences and reputation and has employees, who are qualified to carry out the Contract.

- We hereby declare under criminal and material liability that we have fulfilled liabilities towards our subcontractors resulting from the previous public procurement procedures.

- We hereby declare under criminal and material liability that our company has not, during a period of the last five years, been issued any final legal or administrative decision prohibiting us from carrying out the activity which is the subject of the public tender and have not been convicted of or involved in any criminal proceedings on the grounds of suspicion of committing a criminal offence related to bribery.

- We hereby declare under criminal and material liability that we have not been finally convicted, in any country, for an offence related to our professional conduct.

- We hereby declare under criminal and material liability that we have paid taxes, contributions and other obligatory dues or business obligations in accordance with the regulations of the State where we have the headquarters. We have also paid all overdue business obligations that we have had in the Republic of Slovenia.

- We hereby declare under criminal and material liability that we have settled all our liabilities towards the RTV Slovenija and we are not in a complaint procedures against the RTV Slovenija.

- We hereby declare under criminal and material liability that there are no legal limitations, which should preclude us from signing the Contract.

We hereby agree that the Contracting Authority may, pursuant to the sixth paragraph of Article 42 of the ZJN-2C, exclude our bid from further participation in the public tender procedure if:

- it can prove, on any legal basis, that we committed a serious professional error or severely violated professional rules;

- we gave a misleading interpretation when providing information required under the provisions of Articles 41 to 49 of this Act, in this or any previous procedures, or failed to provide such information.

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

Bidder: ………………………………………………………………

Address: ......................................................................................

## Declaration of the Bidder regarding the spare parts

FOR PUBLIC TENDER JN-B0454 – Lot A

We herewith declare under penal and material responsibility, that we are going to assure the necessary spare parts:

- at least seven (7) years from the date of final acceptance of the vehicle and integrated equipment

which we offered on the public tender JN-B0454, according to the official spare parts price list.

The Contracting Authority will be informed of any change in the official spare parts price list.

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

Bidder: ………………………………………………………………

Address: ......................................................................................

## Declaration of the Bidder regarding the spare parts

FOR PUBLIC TENDER JN-B0454 – Lot B

We herewith declare under penal and material responsibility, that we are going to assure the necessary spare parts:

- at least five (5) years from the date of final acceptance of equipment

which we offered on the public tender JN-B0454, according to the official spare parts price list.

The Contracting Authority will be informed of any change in the official spare parts price list.

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

Bidder: ………………………………………………………………

Address: ......................................................................................

## Declaration of the Bidder – all the offered equipment is factory new

FOR PUBLIC TENDER JN-B0454

We herewith declare, under penal and material responsibility, that all the equipment, offered on the Public Tender JN-B0454, is factory-new.

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

Bidder: ………………………………………………………………..

Address: ......................................................................................

## Declaration of the BIdder regarding the software upgrades

FOR PUBLIC TENDER JN-B0454

We hereby declare, under criminal and material liability, that all the software upgrades for the offered technological equipment, installed in the DSNG Van, will be free of charge for the Contracting Authority within the warranty period.

Place and date: 			Stamp:			             Bidder's official

representative or authorized person

........................................					.........................................................

Manufacturer of the equipment: ..................................................

Address: .......................................................

....................................................................

## STATEMENT OF THE MANUFACTURER

FOR PUBLIC TENDER JN-B0454

We,  …………(the Manufacturer of the equipment )  confirm, that we are acquainted with the contents of Public Tender JN-B0454 (Purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting (by lots), to which ….……  (the Bidder) is going to submit his bid, with the Pro forma Invoice no.: ………

WE DECLARE, that ………… (the Bidder) has full access to the spare parts and replacement equipment for the bidden equipment, according to the requirements from the tender documentation no.JN-B0454.

Place and date: 			Stamp:			             Manufacturer's official

representative or authorized person

........................................					.........................................................

Principal: ..................................................

Address: .......................................................

....................................................................

## STATEMENT OF THE PRINCIPAL

FOR PUBLIC TENDER JN-B0454

We, ………(the Principal of the equipment )  confirm, that we are acquainted with the contents of Public Tender JN-B0454 ( Purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting (by lots)), to which ……………….  (the Bidder) is going to submit his bid, with the Pro forma Invoice no.: ………

WE DECLARE, that ………… (the Bidder) has full access to the spare parts and replacement equipment for the bidden equipment, through our firm, according to the requirements from the tender documentation no. JN-B0454.

As evidence of the aforesaid we enclose the copy of the Contract between us and the Manufacturer of the equipment, wherein it is evident that we have full access to the spare parts and replacement equipment for the bidden equipment.

In case the Contracting Authority subsequently requests the original Contract, we shall present the same for verification.

Place and date: 			Stamp:			             Principal's official

representative or authorized person

........................................					.........................................................

## Sample Contract

Each article in the Contract is written first in Slovenian and then in English language. In case of any doubt or misunderstanding, the Slovenian version should therefore be considered final.

POGODBA ŠTEV.   /  CONTRACT  NO.

JN-B0454

Nakup in integracija DSNG vozila za neposredne prenose preko satelita in javljanja v živo (po sklopih)

Purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting (by lots)

Sklenjena med:

Concluded between:

Radiotelevizija Slovenija, Javni zavod

Kolodvorska 2

1550 Ljubljana

Slovenia

Identifikacijska štev. za DDV / ID V.A.T. No.: SI29865174

Matična štev. / Corporate registry No.:5056497

ki ga zastopa generalni direktor mag. Marko Filli

represented by mag. Marko Filli, the Director General

(v nadaljevanju teksta “NAROČNIK”)

(hereinafter referred to as “CONTRACTING AUTHORITY”)

in / and

……………………………………

……………………………………

……………………………………

……………………………………

Identifikacijska štev. za DDV / ID V.A.T. No.: ……………………………………

Matična štev. / Corporate registry No.: ……………………..

ki ga zastopa …………………………………………………..

represented by …………………………………………………

(v nadaljevanju teksta “PONUDNIK”)

(hereinafter referred to as “BIDDER”)

1. člen

Pogodbeni stranki ugotavljata, da je naročnik izvedel postopek oddaje javnega naročila na osnovi 25. člena Zakona o javnem naročanju – ZJN-2C (Ur. list RS, štev. 18/2011) za:

nakup in integracija DSNG vozila za neposredne prenose preko satelita in javljanja v živo

(po sklopih)

Ponudnik je bil izbran kot najugodnejši ponudnik za sklop………, na osnovi javnega naročila, objavljenega na portalu javni naročil RS, štev. ….., z dne …………  in v Uradnem listu EU, štev. …., z dne ………...

Article 1

The Parties agree that the Contracting Authority carried out the procedure related to the submission of Public Procurement based on Article 25. of the Public Procurement Act (Official Gazette of the Republic of Slovenia, No. 18/2011) for the:

purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting (by lots)

The Bidder has been selected as the most favourable Bidder for Lot….., based on the Public Tender, published in the in the TED of Republic of Slovenia, on … under the no. … and  in the Official Gazette of EU, No. …. on  …

2. člen

S to pogodbo se pogodbeni stranki dogovorita o splošnih in posebnih pogojih izvedbe javnega naročila. Sestavni del te pogodbe so pogoji, določeni z razpisno dokumentacijo štev. JN-B0454, sprejeti in navedeni v ponudbeni dokumentaciji  .............. z dne ……..

Article 2

The Parties agree on general and special conditions related to the realization of the Public Tender. All conditions determined by the Tender documentation no. JN-B0454, adopted and specified in the Bid documentation ….dated   …… shall constitute an integral part of this Contract.

3. člen

3.1

Končna vrednost pogodbe za nakup in integracija DSNG vozila za neposredne prenose preko satelita in javljanja v živo po sklopih:

Sklop A

EUR …………………………. DDP Ljubljana (skladno z INCOTERMS 2000), brez DDV

Sklop B

EUR …………………………. DDP Ljubljana (skladno z INCOTERMS 2000), brez DDV

V primeru plačila domačemu ponudniku, bo le-ta ob izstavitvi računa priračunal 20 % DDV.

V primeru pridobitve blaga znotraj Skupnosti (EU), bo naročnik izvršil samoobdavčitev z DDV, skladno z veljavno zakonodajo o DDV.

V primeru ponudnika izven držav Evropske unije, mora ponudnik na svoje stroške izvršiti tudi uvozno carinjenje ob prihodu pošiljke v Slovenijo in plačati vse uvozne in špediterske dajatve, razen DDV. DDV bo naročnik plačal ob sprostitvi uvoženega blaga v prost promet, skladno z določili Zakona o DDV.

Cene po tej pogodbi so fiksne in se ne smejo spreminjati do konca trajanja te pogodbe.

3.2

Vsi dokumenti, ki jih izda ponudnik, morajo vsebovati tudi oznako javnega naročila oz. pogodbe in oznako naročila. Naročilo bo ponudnik prejel po pričetku veljavnosti pogodbe.

Naročnik bo navedeni znesek plačal na  račun ponudnika štev.:.......................................pri banki: ...........................................................;  v skladu z naslednjimi plačilnimi pogoji:

SKLOP A

- Ponudnik  po dostavi dokazila o nabavljenem vozilu za naročnika, izda račun za prvo (I.) situacijo v vrednosti  20 % pogodbenega zneska.  Naročnik bo ponudniku plačal celotno vrednost prve situacije v 30 dneh po datumu zapisnika, podpisanega s strani naročnika in ponudnika, s katerim bo naročnik potrdil prejem dokazila, da je ponudnik  nabavil ustrezno vozilo za naročnika.

- Ponudnik po drugem ogledu, ki vsebuje tovarniški prevzem, testiranje in zagon DSNG vozila, kar se potrdi z ustreznim zapisnikom, izda račun za drugo (II.) situacijo v vrednosti 60% pogodbenega zneska. Naročnik bo ponudniku plačal celotno vrednost druge  situacije v 30 dneh po datumu zapisnika, podpisanega s strani naročnika in ponudnika o uspešno opravljenem  tovarniškem prevzemu. Račun izstavljen brez ustreznega zapisnika bo zavrnjen.

- Ponudnik z dne uspešno opravljenega končnega prevzema vozila izda račun za tretjo (III.) situacijo v vrednosti 20 % pogodbenega zneska.  Naročnik bo ponudniku plačal celotno vrednost tretje (III.) situacije v  30 dneh po uspešno opravljenem končnem prevzemu  vozila z vgrajeno dodatno opremo in predložitvi zapisnika, podpisanega s strani naročnika.

SKLOP B

- 100 % v roku 30 dni po končnem prevzemu blaga na lokaciji naročnika

Naročnik ne bo predložil garancije za zavarovanje odloženih plačil, kakor tudi ne bo predložil kakšnega drugega instrumenta za zavarovanje plačil.

Article 3

3.1

The total value of the purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting (by lots)  amounts to:

Lot A

EUR …………………………. DDP Ljubljana (accord. to INCOTERMS 2000), without VAT

Lot B

EUR …………………………. DDP Ljubljana (accord. to INCOTERMS 2000), without VAT

In case of a payment to a domestic Bidder, the 20 % VAT shall be added.

In case of a purchase of the goods on the internal EU market, the Contracting Authority shall carry out the reverse charge of VAT, according to the valid Law on VAT.

In case of a Bidder from outside of the European Union, the Bidder has to arrange the import procedure at the departure of the goods to Slovenija. All the customs duties (without VAT)  and costs of forwarding agent are to be borne by the Bidder.  The VAT will be paid by the Contracting Authority after the imported goods have been put on the Slovenian market, according to the provisions of the Law on VAT.

The prices of the equipment according to this Contract are fixed and can not be changed for the period of the Contract duration.

3.2

All documents issued by the Bidder (Invoices, Delivery Notes) shall also incorporate the Public Tender or Contract Number and the Order number. The Bidder will receive the Order after the beginning of the contract validity.

The Contracting Authority shall pay the amount specified in favour of the Bidder’s account No …………………………………… at the Bank ………………………………………………….in accordance with the following payment terms:

LOT A

- After the submission of the evidence on the purchase of the vehicle for the Contracting Authority, the Bidder shall issue the invoice for the first situation (I.) in the amount of 20% of the contractual value. The Contracting Authority will pay the amount of the first situation within 30 days after the acceptance protocol has been signed by the Bidder and the Contracting Authority, by which the Contracting Authority will acknowledge receipt of proof that the Bidder bought the appropriate vehicle for the Contracting Authority.

- After the second visit, which includes technical acceptance, inspection and launch of DSNG vehicle, which must be validated with the acceptance protocol, the Bidder shall issue an invoice for the second situation (II.) in the amount of 60% of the contractual value. The Contracting Authority will pay the amount of the second situation within 30 days after the acceptance protocol of a successful technical acceptance has been signed by the Bidder and the Contracting Authority. An invoice without the acceptance protocol will be rejected.

- After the final acceptance of the vehicle has been successfully carried out, the Bidder shall issue an invoice for the third situation (III.) in the amount of 20% of the contractual value. The Contracting Authority will pay the amount of the third situation within 30 days after the final acceptance of the vehicle with integrated additional equipment has been successfully carried out and after the acceptance protocol has been signed by the Contacting Authority.

LOT B

- 100 % within 30 days after the final acceptance of the goods on location of the Contracting Authority

The Contracting Authority shall not present bank guarantee or any other instrument for insurance of the retained payments.

4. člen

Ponudnik bo izpolnil naročilo v skladu s pogoji ponudbene dokumentacije, ki je sestavni del te pogodbe, v količini, kvaliteti in rokih, sicer bo naročnik unovčil garancijo za dobro izvedbo pogodbenih obveznosti.

Article 4

The Bidder shall fulfil the order according to the terms of the Bid documentation, being the constituent parts of this Contract, in terms of quantities and deadlines required, otherwise the Contracting Authority shall cash-in a performance guarantee.

5. člen

Ponudnik bo blago (opremo) dobavil najkasneje v roku:

SKLOP A  …………………. dni

SKLOP B  …………………..dni

od dneva pričetka veljavnosti te pogodbe.

Po tem roku naročnik lahko unovči garancijo za dobro izvedbo pogodbenih obveznosti.

Ponudnik mora hkrati z opremo ob prevzemu naročniku izročiti še:

- pravilno izpolnjeno dobavnico;

- nalepka dobavitelja z naslednjimi podatki: ime in naslov dobavitelja, številka pogodbe, datum dobave in trajanje garancije;

- tehnično dokumentacijo in navodila za uporabo in servisiranje;

- licence, dokumentacijo in medije za vgrajeno programsko opremo;

- druge dokumente;

sklop A: dokument o homologaciji

sklep o ustreznosti opreme skladno s pravilnikom o ugotavljanju skladnosti in odobravanju terminalske opreme in radijskih postaj, po UL RS št.50/97

Article 5

Bidder shall supply the goods (equipment) at the latest within:

LOT A …………………………. days

LOT B …………………………. days

after the Contract validity date.

After this delivery deadline the Contracting Authority may cash-in a performance guarantee.

The bidder is obliged to provide with the delivery the following documents:

- properly completed delivery note

- label of the supplier with the following information: name and address of the supplier, the contract number, delivery date and duration of the warranty

- technical documentation, user and maintenance manuals

- licences, documentation, media for software included

- other documents:

Lot A: homologation certificate

Certificate of meeting the requirements as set in the Regulations on Technical Requirements for Radio Equipment published in the Official Gazette of the Republic of Slovenia No.50/97 from year 1997

6. člen

Garancijski pogoji so navedeni v ponudbeni dokumentaciji, ki je sestavni del te pogodbe in so bili sprejeti s strani obeh pogodbenih partnerjev.

SKLOP A

Garancijski pogoji za sklop A

Garancijski rok za vozilo v sklopu A:

- ……….mesecev 			za dele, gibljive sklope z omejitvijo 100 000 km

- ……….let				za barvo na vozilu

- ……….let				za predelavo karoserije, na prerjavenje

Garancijski roki za opremo, ponujeno v ponudbi in vgrajeno v vozilo za sklop A morajo  biti enaki ali daljši od rokov, ki jih za to opremo zagotavljajo proizvajalci posamezne opreme, vendar najmanj 2 leti od dneva končnega prevzema vozila z pripadajočo opremo sklopa A.

Ponudnik mora predložiti svojo lastno izjavo s podrobnejšimi podatki o garancijskem vzdrževanju vozila in opreme, iz katerih morajo biti razvidni:

- Naslov, telefonska številka in e-mail strokovnjaka za servisiranje, ki svetuje serviserju naročnika v času garancije ob odpravljanju napake ………………………………………………………..

- Lokacijo evropskega skladišča vseh nadomestnih delov, kontaktno osebo, e-mail naslov in številko faxa za naročilo nadomestnih delov……………………………………………………..

- Odzivni čas in rok, v katerem bo napaka odpravljena oz. v katerem bo ponudnik naročniku zagotovil nadomestno opremo …………………………………………………………………….

Ponudnik zagotavlja:

- Za čas garancije:  brezplačno odposlanje nadomestnih delov s hitro pošto v roku 24 ur po zahtevi, upoštevajoč delovne dni v tednu. Zahteva naročnika bo poslana preko elektronske pošte in fax sporočila.  Naročnik bo vrnil pokvarjeni del po prejetju nadomestnega. Ponudnik zagotavlja brezplačno nadgradnjo programske opreme v času garancije, razen za opremo, ki jo je naročnik dostavil ponudniku za vgradnjo.

- Za čas po poteku garancije :  ponudnik zagotavlja odpošiljanje  nadomestnih delov s hitro pošto v roku 48 ur po zahtevi, upoštevajoč delovne dni. Zahteva naročnika bo poslana preko elektronske pošte in fax sporočila.  Naročnik bo vrnil okvarjeni del po prejetju nadomestnega in ga plačal v 30 dneh po prejetju računa.

SKLOP B

Garancijski pogoji za sklop B

Garancijski roki za opremo, ponujeno v ponudbi za sklop B morajo  biti enaki ali daljši od rokov, ki jih za to opremo zagotavljajo proizvajalci posamezne opreme, vendar najmanj 2 leti od dneva končnega prevzema opreme.

Ponudnik mora predložiti svojo lastno izjavo s podrobnejšimi podatki o garancijskem vzdrževanju  opreme, iz katerih morajo biti razvidni:

- Naslov, telefonska številka in e-mail strokovnjaka za servisiranje, ki svetuje serviserju naročnika v času garancije ob odpravljanju napake ……………………………………………………….

- Lokacijo evropskega skladišča vseh nadomestnih delov, kontaktno osebo, e-mail naslov in številko faxa za naročilo nadomestnih delov …………………………………………………….

- Odzivni čas in rok, v katerem bo napaka odpravljena oz. v katerem bo ponudnik naročniku zagotovil nadomestno opremo …………………………………………………………………….

Ponudnik zagotavlja:

- Za čas garancije:  brezplačno odposlanje nadomestnih delov s hitro pošto v roku 24 ur po zahtevi, upoštevajoč delovne dni v tednu. Zahteva naročnika bo poslana preko elektronske pošte in fax sporočila.  Naročnik bo vrnil pokvarjeni del po prejetju nadomestnega.

- Za čas po poteku garancije :  ponudnik zagotavlja odpošiljanje nadomestnih delov s hitro pošto v roku 48 ur po zahtevi, upoštevajoč delovne dni. Zahteva naročnika bo poslana preko elektronske pošte in fax sporočila.  Naročnik bo vrnil okvarjeni del po prejetju nadomestnega in ga plačal v 30 dneh po prejetju računa.

Garancijski pogoji so navedeni v ponudbeni dokumentaciji, ki je sestavni del te pogodbe in so bili sprejeti s strani obeh pogodbenih partnerjev.

Article 6

The guarantee terms are determined in the Bid documentation, which shall constitute the integral part of this Contract and have been adopted by both Parties.

Warranty conditions for the Lot A:

The warranty period for the vehicle in the Lot A:

- ………. months 			for units and mechanisms with 100.000 km mileage limit

- ………. years				for the paint on the vehicle

- ………..years				for bodywork anti-perforation

The warranty period for the equipment offered in the Bid for the Lot A and integrated in the vehicle must be equal or longer than the warranty period offered from the direct manufacturers of offered equipment , but at least two (2) years from the successful final acceptance of the vehicle with integrated equipment under lot A.

The Bidder must enclose his own statement with the detailed information on the maintenance of equipment in warranty period, according to the requirements, stated in the chapter “Warranty conditions” in the TECHNICAL PART of Tender documentation, from which must be evident:

- The address, phone and e-mail of the servis expert who advices during the warranty period ……………………………………………………………………………………………………………………

- the address of the European service for bidden equipment, contact person, phone and fax number

……………………………………………………………………………………………………………………

- response time and the time period when the error will be eliminated or time period when the Bidder will ensure the replacement equipment ……………………………………………………………………..

The Bidder in his statement must ensure:

For the warranty period: the dispatch of the replacement module by express courier service within 24 hours  (within the  working days),  from the receipt of the Contract Authority’s report by fax or e-mail. The Contracting Authority will return the defective module after receipt of the replacement one.

The Bidder must ensure that all the software upgrades for the offered technological equipment, installed in the DSNG van, will be free of charge for the Contracting Authority within the warranty period, except for the equipment delivered for integration from the Contracting Authority.

- For the after warranty period: the dispatch of the replacement module by express courier service within 48 hours  (within the  working days),  from the receipt of the Contract Authority’s report by fax or e-mail. The Contracting Authority will return the defective module after receipt of the replacement one and will pay it within 30 days after receipt of  the invoice.

Warranty conditions for the Lot B:

The warranty period for the equipment offered in the Bid for the Lot B must be equal or longer than the warranty period offered from the direct manufacturers of offered equipment , but at least two (2) years from the successful final acceptance of the  equipment under lot B.

The Bidder must enclose his own statement with the detailed information on the maintenance of equipment in warranty period, according to the requirements, stated in the chapter “Warranty conditions” in the TECHNICAL PART of Tender documentation, from which must be evident:

- The address, phone and e-mail of the servis expert who advices during the warranty period ……………………………………………………………………………………………………………………

- the address of the European service for bidden equipment, contact person, phone and fax number…………………………………………………………………………………………………………..

- response time and the time period when the error will be eliminated or time period when the Bidder will ensure the replacement equipment ……………………………………………………………………..

The Bidder in his statement must ensure:

- For the warranty period: the dispatch of the replacement module by express courier service within 24 hours  (within the  working days),  from the receipt of the Contract Authority’s report by fax or e-mail. The Contracting Authority will return the defective module after receipt of the replacement one.

- For the after warranty period: the dispatch of the replacement module by express courier service within 48 hours  (within the  working days),  from the receipt of the Contract Authority’s report by fax or e-mail. The Contracting Authority will return the defective module after receipt of the replacement one and will pay it within 30 days after receipt of  the invoice.

7. člen

SKLOP A

Končni prevzem vozila in operativno – vzdrževalni tečaj na lokaciji naročnika

Ponudnik mora vozilo z vgrajeno dodatno opremo dobaviti na lokacijo naročnika RTV

Slovenija v Ljubljani.

- Kosovni prevzem po dobavi DSNG vozila opravi naročnik  najkasneje v roku 5 delovnih dni po dobavi vozila z vgrajeno opremo na lokacijo naročnika v Ljubljani. S kosovnim prevzemom naročnik ugotavlja kompletnost vozila.

- Končni prevzem DSNG vozila opravi naročnik  najkasneje v roku 21 delovnih dni po uspešno opravljenem kosovnem prevzemu.

Naročnik bo v postopku končnega prevzema ugotovil, ali vsa oprema deluje v skladu z v razpisnih pogojih zahtevanimi tehnološkimi in funkcionalnimi lastnostmi. Ob končnem prevzemu opreme je lahko prisoten predstavnik ponudnika.

Vse morebitne nepravilnosti, ugotovljene pri končnem prevzemu opreme, morajo biti odpravljene s strani ponudnika v roku 21 dni, v nasprotnem primeru  ima naročnik pravico unovčiti garancijo za dobro izvedbo pogodbenih obveznosti.

Šteje se, da je končni prevzem opravljen takrat, ko so odpravljene vse morebitno ugotovljene nepravilnosti, ki jih mora naročnik specificirati v pisni obliki.

Z dnem uspešno opravljenega končnega prevzema opreme prične teči garancijski rok.

- Ponudnik bo izvedel operativno-vzdrževalno izobraževanje v trajanju vsaj 2 dni po po 8 ur/dan za 6 - 8 udeležencev naročnika po končnem prevzemu vozila na lokaciji naročnika.

Ponudnik nosi vse stroške izpeljave šolanja (t.j. vse stroške v  zvezi s  šolanjem, literaturo in pripomočki za izvedbo šolanja, kakor tudi stroške prevoza in nastanitve za predavatelja.

Šolanje mora obvezno vsebovati naslednje:

  - obrazložitev delovanja sistema električnega napajanja vozila

  - obrazložitev delovanja vseh stopenj  RF oddajne in sprejemne verige

  - obrazložitev nastavljanja in optimiranja posameznih sklopov,

praktično nastavljanje optimalnega delovanja in uglaševanja, obrazložitev meritev s praktičnim delom, ki jih mora vsak udeleženec izvesti lastnoročno,

  - navodila in predlogi za iskanje napak in ponovnega zagona posameznih funkcij s praktičnim delom vsakega posameznega udeleženca,

- končno preverjanje znanja in podelitev certifikata za operativno uporabo in osnovno diagnosticiranje napak in popravilo enostavnih napak na sistemih v DSNG vozilu.

Šolanja in pripadajoče gradivo mora biti v slovenskem ali v angleškem jeziku.

Stroške izvedbe operativno-vzdrževalnega izobraževanja je ponudnik vključil v ceno.

Naročnik si pridržuje pravico zmanjšati ali povečati število udeležencev in/ali dni šolanja glede na potrebe.

Cena dodatnega dneva šolanja ni vključena v osnovno ponudbo.

SKLOP B

Končni prevzem oddajno-sprejemne opreme

Kosovni prevzem opreme bo naročnik opravil v skladišču RTV Slovenija v Ljubljani, najkasneje v roku treh (3) dneh od dneva dobave.

S kosovnim prevzemom se ugotavlja celovitost dobavljene opreme.

Naročnik bo opravil končni prevzem dobavljene opreme najkasneje v roku sedmih (7) dneh po kosovnem prevzemu opreme.

Naročnik bo v postopku končnega prevzema ugotovil, ali vsa oprema deluje v skladu z v razpisnih pogojih zahtevanimi tehnološkimi in funkcionalnimi lastnostmi. Ob končnem prevzemu opreme je lahko prisoten predstavnik ponudnika.

Vse morebitne nepravilnosti, ugotovljene pri končnem prevzemu opreme, morajo biti odpravljene s strani ponudnika v roku 21 dni, v nasprotnem primeru  ima naročnik pravico unovčiti garancijo za dobro izvedbo pogodbenih obveznosti.

Šteje se, da je končni prevzem opravljen takrat, ko so odpravljene vse morebitno ugotovljene nepravilnosti, ki jih mora naročnik specificirati v pisni obliki.

Z dnem uspešno opravljenega končnega prevzema opreme prične teči garancijski rok.

Article 7

LOT A

Final acceptance and operational-maintenance training on the RTVSLO location

The bidder has to deliver the vehicle with installed equipment  to the location of the Contracting Authority RTV Slovenija in Ljubljana.

- The quantity acceptance will be done in 5 working days after the delivery of the DSNG van with installed equipment to the location of RTVSLO in Ljubljana. With the quantitative acceptance the Contracting Authority will determine completeness of the vehicle regarding contract agreement.

- The final acceptance of the DSNG van must be completed by the Contracting Authority within twenty one (21) days after the date of successfully quantitative acceptance.

The Contracting Authority shall determine with the final acceptance whether the equipment is working according to the requested technical and functional requirements in tender documentation. At this final acceptance the representatives of the Bidder can be present.

All eventual incorrectness, ascertained at final acceptance procedure, are to be eliminated by the Bidder within 21 days, after this delivery deadline the Contracting Authority may cash-in a performance guarantee, and the Bidder must submit a new Performance Guarantee.

It is understood that the final acceptance will be completed when all eventual incorrectness are eliminated. The incorrectness is to be specified in writing by the Contracting Authority.

The warranty time starts on the day of signing the final acceptance.

- The contracting authority require the operational-maintenance training for the 6-8  users of the DSNG van in duration of at least 2 days per 8 hours after the final acceptance on location of the contract authority.

The bidder had to cover all the expenses for the training ( expenses for the literature,  any cost connected to the training, accommodation, travel expenses for the lecturer).

The training must include the following:

- explanation of the operation of powering system in the vehicle,

- explanation of the operation of all stages of RF transmitting and receiving chain,

- explanation of adjustments, optimizing, measurements of individual stages, practical adjustments for optimal operation, tuning,  each participant must personally perform those settings,

- instructions and suggestions for error finding and re-launch of individual functions (each participant must personally perform those tasks),

- final examination and granting of a certificate for operational work, fault finding and simple faults repair on systems of DSNG van.

Education and related material must be in the Slovenian or English language.

The expenses for the operational-maintenance training must be included in the basic offer.

The Contracting Authority reserves the right to reduce or increase the number of participants and/or days of schooling in terms of the number and complexity of the equipment.

The price of additional day of training, is not include in the price of the basic offer.

LOT B

Final acceptance of the transmitting-receiving equipment

The quantitative acceptance will be done in the warehouse of RTV Slovenija, Čufarjeva Street 6, Ljubljana within three (3) working days after the equipment is delivered to the warehouse of RTV Slovenija.

With the quantitative acceptance the Contracting Authority will determine completeness of equipment regarding contract agreement.

The final acceptance of the delivered goods (equipment) must be completed by the Contracting Authority within seven (7) days after the date of quantitative acceptance.

The Contracting Authority shall determine with the final acceptance whether the equipment is working according to the requested technical and functional requirements in tender documentation. At this final acceptance the representatives of the Bidder can be present.

All eventual incorrectness, ascertained at quantitative acceptance procedure, are to be eliminated by the Bidder within 21 days, after this delivery deadline the Contracting Authority may cash-in a performance guarantee.

It is understood that the final acceptance will be completed when all eventual incorrectness are eliminated. The incorrectness is to be specified in writing by the Contracting Authority.

The warranty time starts on the day of signing the final acceptance.

8. člen

SKLOP A

Ponudnik se obvezuje, da bo v dobi zagotavljanja rezervnih delov (sedem let po končnem prevzemu), dobavljal le-te skladno z uradnim cenikom ponudnika.

Ponudnik mora o vsaki spremembi uradnega cenika rezervnih delov obvestiti naročnika.

SKLOP B

Ponudnik se obvezuje, da bo v dobi zagotavljanja rezervnih delov (pet let po končnem prevzemu opreme), dobavljal le-te skladno z uradnim cenikom ponudnika.

Ponudnik mora o vsaki spremembi uradnega cenika rezervnih delov obvestiti naročnika.

Article 8

LOT A

The Bidder is obliged that he shall assure the necessary spare parts  in the period of at least seven (7) years from the date of final acceptance of equipment, according to the official spare parts price list.

The Contracting Authority will be informed of any change in the official spare parts price list.

LOT B

The Bidder is obliged that he shall assure the necessary spare parts in the period of at least five (5) years from the date of final acceptance of equipment, according to the official spare parts price list.

The Contracting Authority will be informed of any change in the official spare parts price list.

9. člen

Naročnik lahko oporeka kakovosti blaga v zakonsko določenih rokih po tem, ko ugotovi neustrezno kakovost. V garancijskem roku pa lahko vsak čas zahteva odpravo napake, ki jo je ponudnik dolžan odpraviti. Pogoji odpravljanja napak so navedeni v ponudbeni dokumentaciji, ki je sestavni del te pogodbe. V primeru, da kakovost blaga ni v skladu z zahtevami razpisne dokumentacije ali iz ponudbene dokumentacije, bo naročnik unovčil garancijo za dobro izvedbo pogodbenih obveznosti.

Ponudnik  odgovarja za  skrite napake na dobavljenem blagu. Skrite napake so tiste , ki  jih  naročnik ni mogel odkriti  z  običajnim pregledom  dobavljenega blaga. Naročnik mora obvestiti  ponudnika o napaki v osmih dneh, šteto od dneva, ko je napako opazil.

Article 9

After the Contracting Authority has established the inappropriate quality of goods, this quality of goods may be contested in statutory deadlines. During the guarantee period the elimination of defects can be requested at any time and the Bidder shall be liable to remedy any defect. Terms related to the remedy of defects are determined in the Bid documentation, which constitute an integral part of this Contract. If the quality of goods is not in accordance with the stipulations of the tender or bid documentation, the Contracting Authority shall cash-in a performance guarantee.

The Bidder is responsible for the hidden errors on the delivered goods. Hidden errors are those, the Contracting Authority was unable to determine with the commonly performed examination of the delivered goods. The Contracting Authority shall inform the Bidder about the hidden error within eight days, counting from the date the hidden error had been noticed.

10. člen

Če dobava ni realizirana v predvidenem roku po ponudnikovi krivdi, razen v primeru višje sile, je ponudnik dolžan plačati naročniku kazen v višini 1 odstotek vrednosti dobave, ki predstavlja funkcionalno enoto, za vsak zaključen teden, vendar ne več kot 5 odstotkov celotne pogodbene vrednosti.  Kazen začne teči  naslednji delovni dan po določenem času dobave.

Če dobava zaostaja po ponudnikovi krivdi za več kot 6 tednov, ima naročnik pravico, razen če uveljavlja kazenski zahtevek, da določi nov dobavni rok ali prekine pogodbo.

Article 10

If the goods are not supplied due to the Bidder’s fault in a planned timescale, with the exception of Force Majeure, the Bidder shall be liable to pay penalties in the amount of 1 per cent of a respective partial delivery, incorporating a functional unit, for each week completed, but not increasing 5 per cent of the total Contract amount. The penalty shall commence next working day after the delivery deadline determined.

If the delivery is delayed due to Bidder’s fault for more than 6 weeks, the Contracting Authority shall have right, unless the penal claim is exercised, to determine a new delivery time or to terminate the Contact.

11. člen

Ponudnik je skladno z določili razpisne dokumentacije štev. JN-B0454 ponudil ločeno od osnovne ponudbe:

za sklop A naslednje opcijske ponudbe: 3.2.2 OP1, 3.2.3 OP2

za sklop B naslednje opcijske ponudbe: 3.3.2 OP3, 3.3.3 OP4, 3.3.4 OP5.

Cene opcijskih ponudb so fiksne do še eno leto od pričetka veljavnosti osnovne pogodbe.

V primeru, da se bo naročnik odločil za katero koli od opcij že ob odločitvi o oddaji javnega naročila, jo/jih bosta  pogodbeni stranki vključili v osnovno pogodbo. Če pa se bo naročnik odločil za katero koli od opcij kasneje (v roku do enega leta od pričetka veljavnosti osnovne pogodbe, glede na dejanske potrebe in razpoložljiva finančna sredstva), bosta pogodbeni stranki skladno s temi opcijskimi ponudbami sklenili Dodatek k pogodbi JN-B0454.

Article 11

The Bidder offered according to the stipulations of the tender documentation no. JN-B0454, separately from the basic offer also the following optional offers:

for LOT A: 3.2.2 OP1, 3.2.3 OP2

for LOT B: 3.3.2 OP3, 3.3.3 OP4, 3.3.4 OP5.

The prices of optional offers are fixed one year from the beginning of the Contract validity.

In case the Contracting Authority decides for the purchase of one or more of these options already at the Decision time on the award of a Contract, the same will be included in the basic Contract. In case the Contracting Authority decides for the purchase of these options later (in the period up to one year from the beginning of the Contract validity, subject to available financial resources and actual needs), the contractual parties shall conclude an Annex to the Contract JN-B0454.

12. člen

Pogodbeni stranki se obvezujeta, da bosta naredili vse, kar je potrebno za izvršitev pogodbe in da bosta ravnali kot dobra gospodarja. Vse  morebitne spore v zvezi s to pogodbo bosta stranki najprej poizkušali rešiti po mirni poti. Če razrešitev po mirni poti ne bo mogoča, sta pogodbeni stranki  sporazumni, da je za reševanje vseh morebitnih sporov iz te pogodbe pristojno sodišče v Ljubljani po slovenskem pravu.

Article 12

The Parties undertake to exercise their best efforts to implement the Contract and act with due diligence. The Parties shall endeavour to resolve all eventual disputes arising out of this Contract by mutual agreement. Should such amicable settlement not be substantially reached, the Parties agree to refer, the dispute arising out of this Contract, to the Court of Ljubljana, according to the Slovenian law.

13. člen

V primeru višje sile kot so požar, poplava, potres, vojna, stavke in podobno, se lahko naročnik in ponudnik sporazumeta za podaljšanje roka izpolnitve po tej pogodbi, za dobo trajanja višje sile. Če zaradi daljših rokov trajanja višje sile ne bi bilo mogoče izpolniti pogodbenih obveznosti, lahko pogodbeni stranki pogodbo prekineta. Prekinitev ali podaljšanje  pogodbe mora biti v pisni obliki. V primeru daljšega trajanja višje sile pogodbeni stranki lahko pogodbo razdreta, vsaka stranka nosi svoje, do razdrtja pogodbe nastale stroške.

Article 13

In the event of Force Majeure such as fire, flood, earthquake, war, strikes and similar, the Contracting Authority and the Bidder agree to extend the period that its performance of such obligations is prevented by the event of Force Majeure. Should it not be possible to fulfil obligations under this Contract in spite of all longer periods of time, the Parties may terminate the Contract. The termination or extension of the Contract shall be provided in writing. In the case of longer period of Force Majeure the Parties may terminate the Contract, each party bearing their own costs, that have been occurred till then.

14. člen

Pogodba je sklenjena z odložnim pogojem in stopi v veljavo:

- z dnem obojestranskega podpisa  s strani pooblaščenih podpisnikov naročnika in ponudnika ter veljavnim žigom obeh pogodbenih strank;

- s predložitvijo garancije za dobro izvedbo pogodbenih obveznosti (izdane s strani banke ali zavarovalnice), brezpogojne, nepreklicne in plačljive na prvi poziv, v višini 10 % pogodbene vrednosti in z veljavnostjo še šest mesecev po pogodbeno določenem datumu dobave opreme. Ponudnik je dolžan predložiti garancijo za dobro izvedbo pogodbenih obveznosti najkasneje 10 dni po podpisu pogodbe.

Article 14

The agreement is made under the suspense and enters into force:

- on the day the authorized representatives of the Contracting Authority and Bidder affix their signatures and valid stamps of both parties;

- by Bidder’s presentation of the  Performance Guarantee (issued by Bank or Insurance Company), irrevocable, unconditional and payable at first call in the amount of 10 % of the Contractual value and valid six months after confirmed delivery of the equipment. The Bidder must present the Performance Guarantee at the latest 10 days after the signature of the Contract.

15. člen

Določila pogodbe so fiksna in se jih ne sme spreminjati v času trajanja pogodbe. V primeru, da nastanejo izredni pogoji, ki bi onemogočali izpolnjevanje pogodbenih določil, lahko stranki skleneta dodatek k pogodbi v pisni obliki. Ta mora biti podpisan in žigosan s strani obeh pooblaščenih pogodbenih predstavnikov.

Article 15

The provisions of the Contract are fix and can not be amended during the duration of the Contract. In the event of extraordinary conditions that should preclude the fulfilment of the Contract provisions, the Parties may conclude the Annex to the Contract in writing. This Annex must be signed and duly stamped by the authorized representatives of the Parties.

16. člen

Pogodbeni stranki izjavljata , da je to pogodbo možno odpovedati pred  njeno izpolnitvijo  v primeru, da nastopi  ena od  naslednjih spodaj navedenih  okoliščin.

Naročnik  lahko odpove pogodbo pred njeno izpolnitvijo :

- če je proti  ponudniku uveden stečaj ali prisilna poravnava,

- če je neuspešno pretekel  pogodbeno določen rok, pa ponudnik ni izpolnil pogodbenih obveznosti,

- če ponudnik  ni odpravil ugovarjanih napak  oz. odprava napak ni možna,

Ponudnik lahko odpove pogodbo :

- če naročnik ne plača  pogodbene cene.

Odpoved pogodbe se poda v pisni obliki, pogodba preneha veljati  v petnajstih  dneh   po prejemu takšne odpovedi, podpisane s strani pooblaščene osebe pogodbenega stranke.

Če odpove pogodbo naročnik, lahko zahteva povrnitev škode, ki mu je nastala zaradi neizpolnitve pogodbe s strani ponudnika. Če odpove pogodbo  ponudnik, lahko zahteva plačilo za že opravljene storitve do dneva odpovedi pogodbe. Odškodninski zahtevki pogodbeno zveste stranke s tem niso izključeni.

Article 16

The Contract parties declare this contract could be terminated before its fulfilment only if one of the following circumstances occurred.

The Contracting Authority is justified to terminate the contract before its fulfilment if:

- the compulsory settlement, bankruptcy or liquidation procedures are initiated against the  Bidder,

- the contractual delivery date is expired  and the Bidder 's obligations are not fulfilled,

- the Bidder does not eliminate the defects or the elimination of the defects is not possible.

The Bidder is justified to terminate the contract if:

- the Contracting Authority does not pay the contractual price.

The termination of the Contract shall be provided in writing, the contract ceases to be valid fifteen days from the receipt of such termination, signed by the authorized person of either party. If the Contract is terminated by the Contracting Authority, the Bidder is liable to reimburse the damage, caused due to his non-fulfilment of the Contract.  If the Contract is terminated by the Bidder, he is justified to require the payment for contractual works already done till the date of the contract termination. By this the indemnity claims of contractual loyal party are not  excluded.

17. člen

S strani naročnika je za izvajanje pogodbe odgovoren …. (telefon: +386 1 475 ….), s  strani ponudnika pa: …. (telefon: ….).

Article 17

Each party shall nominate representatives, responsible for the  realization of the Contract, i.e.: for the Contracting Authority (phone: +386 1 475  ; for the Bidder: _______________ (phone: +___________)

18. člen

Pogodba je sestavljena iz naslednjih delov, ki predstavljajo enovito celoto:

- Osnovna pogodba s komercialnimi pogoji,

- Priloga 1 – Ponudbena dokumentacija štev. ............................................................

- Priloga 2 – Garancija za dobro izvedbo pogodbenih obveznosti

Vsak člen pogodbe je najprej napisan v slovenskem jeziku, nato pa še v angleškem jeziku. V primeru kakršnegakoli dvoma ali napačne razlage, velja slovenska verzija.

Pogodba je sestavljena v petih izvodih, od katerih prejme naročnik tri izvode, ponudnik pa dva izvoda.

Article 18

The Contract encompass the following parts, which represent the uniform whole:

- Basic Contract including commercial terms, Slovenian and English version

- Enclosure 1 - Bid documentation …..No.   …………

- Enclosure 2 - Performance Guarantee

Each article in the Contract is written first in Slovenian and then in English language. In case of any doubt or misunderstanding, the Slovenian version should therefore be considered final.

The Contract is drawn up in five copies, the Contracting Authority receiving three copies, and the Bidder two copies.

PODPIS IN ŽIG POOBLAŠČENIH PREDSTAVNIKOV NAROČNIKA IN PONUDNIKA – POGODBA ŠT. JN-B0454

THE SIGNATURE AND SEAL OF THE AUTHORIZED REPRESENTATIVES OF THE CONTRACTING AUTHORITY AND BIDDER – CONTRACT No. JN-B0454

Ljubljana, …....................	………….., …….…................

NAROČNIK: /	PONUDNIK: /

CONTRACTING AUTHORITY:	BIDDER:

Radiotelevizija Slovenija, Javni zavod	…………………………………..

Generalni direktor / Director General	…………………………………..

mag. Marko Filli	…………………………………..

Žig / Stamp:	Žig / Stamp:

Place and date....................................

Beneficiary……………………..

## Guarantee for the seriousness of Bid No...... – FOR LOT A ONLY

In accordance with the public procurement, published in  the Official Gazette of the Republic of Slovenia, no. …..,  dated ………, for purchase of the following goods (services):

1…………………………..

2…………………………..

3…………………………..

for the purposes of the Contracting Authority (i.e. Beneficiary), the Bidder ………………………………. is bound to submit to the Contracting Authority a guarantee for seriousness of the bid to the amount of ………….  EUR.

The Bank is bound to pay stated amount in the following events:

a)  the Bidder withdraws or changes his bid within its term of validity

or

b)  the Bidder, selected at public selection of bids:

- does not fulfil or withdraws from signing a contract in accordance with tender documentation

or

- does not submit or refuses to submit a Performance Bank Guarantee in accordance with tender documentation.

We are bound to pay within 15 days after the receipt of the first written demand by Contracting Authority the above mentioned amount without any additional grounding if the Contracting Authority in it’s claim states, that it is entitled to demanded amount due to fulfilment of one or two above mentioned events and if the Contradicting Authority states, to which event it refers.

Claim for above reason must be presented to the Bank and must contain:

1. original summons of Contracting Authority for cashing-in the Bank guarantee in accordance with

above paragraph and

2. original Guarantee no. ../……………..

With every payment on this guarantee the sum of guarantee is reduced by the same amount.

This guarantee is valid until the Bidder is chosen according to the above mentioned public procurement and (in case the correct or partly correct offer is accepted) until the Contract between chosen Bidder and Contracting Authority is signed and Performance Guarantee being presented by the chosen Bidder, but not later than the Bid expiration date .

We have to receive your claims for cashing-in of the amount guaranteed until 12 September, 2011 at the latest. After this term the validity of guarantee is automatically terminated irrespective of whether or not the guarantee is returned to the bank.

This guarantee is not transferable.

Eventual dispute between Beneficiary and the Bank will be settled by the Court of Ljubljana, according to the Slovenian law.

Bank

(stamp and signature)

Name of the Bidder: …………………………………………………………………

Address of the Bidder: ………………………………………………………………

## STATEMENT regarding the Performance Guarantee

FOR PUBLIC TENDER JN-B0454

Should we, .................. (The Bidder) be awarded the Tender of RTV Slovenija, No. JN-B0454

Purchase and integration of DSNG vehicle for direct transmission by satellite and live reporting (by lots)

WE DECLARE,

we will supply a Performance Bank Guarantee for 10 % of the contractual value upon Contract signature. The Performance Guarantee will be issued by the first class Bank or Insurance Company and will be irrevocable, unconditional and payable at first call, valid 6 more months after the confirmed delivery date.

Place and date: 	Stamp:	Signature of the Bidder’s

authorized person

………………………………		………………………………

Radiotelevizija Slovenija, Javni zavod,

Commercial Department

e-mail: javna.narocila@rtvslo.si

Fax No..: + 386 1  475 2186

Date: .............................................................

## Explanation of the Tender documentation No. JN-B0454

1. Questions:

..................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................

2. Answers:

...................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................................